## Slide 1: Chapter 1-3 Course Implementation
计算机科学与技术学院
School of Computer Science and Technology
计算机系统概论
Introduction to Computing Systems
（ CS1002A.01 ）

## Slide 2: Outline
Course and Crew
1
Computer is in Everything!
2
Why Take This Course?
3
Great Ideas in Computing Systems
4
What’s This Course All About ?
5
Summary
6

## Slide 3: Text Book
Introduction to computer architecture(ISA)
  How is data represented?
  What are the pieces of a computer?
  How do computers work?
Programming
  How do I "talk" directly to the machine?-Assembly language
  How do I program in “C”?-high level language(HLL)
Computer systems and computation
  How do simple HW/SW elements come together to realize complex computations?
Introduction to Computing Systems: from bits and gates to C/C++and beyond(3nd edition),
Yale N. Patt and Sanjay J. Patel， September 2019, McGraw-Hill Higher Education

## Slide 4: Text Book 参考资料 by Patt
工具和习题
  https://highered.mheducation.com/sites/1260150534/student_view0/
试卷和参考 EE 306 - Exams (utexas.edu)
  https://users.ece.utexas.edu/~patt/21f.306/exams.html
Introduction to Computing Systems: from bits and gates to C/C++and beyond(3nd edition),
Yale N. Patt and Sanjay J. Patel， September 2019, McGraw-Hill Higher Education

## Slide 5: Text Book Components
Part 1: Hardware(Chapter 1-4)
  Representing data,
  transistors,
  gates,
  digital logic structures
  von Neumann machine model
Part 2: Software: Assembly language(Chapter 5-10)
  Instructions,
  (structured) programming,
  input/output,
  relationship to hardware
Part 3: Software: C programming(Chapter11-19), selected
  Syntax, operators, control structures, functions, pointers, recursion, data structures, relationship to assembly language
  Assume already familiar with programming (C)

## Slide 6: This Course Focus on
Chapt 2 Bits, Data Types, and Operations
  How do we represent information using electrical signals?
Chapt 3 Digital Logic Structures
  How do we build circuits to process information?
Chapt 4, 5,6 Computer Machine Model, Processor and Instruction Set
  How do we build a processor out of logic elements?
  What operations (instructions) will we implement?
Chapt 7 Assembly Language Programming
  How do we use processor instructions to implement algorithms?
  How do we write modular, reusable code? (subroutines)
Chapt 8 Data Structures
Chapt 9 I/O, Traps, and Interrupts
  How does a processor communicate with outside world?
Chapt 11, C Implementation related to hardware

## Slide 7
Abstraction Layers in Modern Systems
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics
Application

## Slide 8: Transformations Between Layers
How do we solve a problem using a computer? A systematic sequence of transformations between layers of abstraction.
Problem
Algorithm
Program
Software Design:
choose algorithms and data structures
Programming:
use language to express design
Instr Set
Architecture
Compiling/Interpreting:
convert language to machine instructions
Notes: 8
算法（Algorithm）是指解题方案的准确而完整的描述，是一系列解决问题的清晰指令，算法代表着用系统的方法描述解决问题的策略机制。也就是说，能够对一定规范的输入，在有限时间内获得所要求的输出。如果一个算法有缺陷，或不适合于某个问题，执行这个算法将不会解决这个问题。不同的算法可能用不同的时间，空间或效率来完成同样的任务。一个算法的优劣可以用空间复杂度与时间复杂度来衡量。

## Slide 9: Deeper and Deeper…
Instr Set
Architecture
Microarch
Circuits
Processor Design:
choose structures to implement ISA
Logic/Circuit Design:
gates and low-level circuits to implement computer components
Devices
Process Engineering & Fabrication:
develop and manufacture lowest-level components
Notes: 9

## Slide 10: Descriptions of Each Level
Problem Statement
  stated using "natural language"
  may be ambiguous, imprecise
Algorithm
  step-by-step procedure, guaranteed to finish
  definiteness, effective computability, finiteness
Program
  express the algorithm using a computer language
  high-level language, low-level language
Instruction Set Architecture (ISA)
  specifies the set of instructions the computer can perform
  data types, addressing mode

## Slide 11: Descriptions of Each Level (cont.)
Microarchitecture
  detailed organization of a processor implementation
  different implementations of a single ISA
Logic Circuits
  combine basic operations to realize microarchitecture
  many different ways to implement a single function (e.g., addition)
Devices
  properties of materials, manufacturability
Notes: 11

## Slide 12: Many Choices at Each Level
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Tradeoffs:
cost
performance
power
(etc.)
Notes: 12
Sun and Java are trademarks of Sun Microsystems, Inc. SPARC is a trademark of SPARC International, Inc. Intel and Pentium are trademarks of Intel Corporation. IBM and PowerPC are trademarks of IBM Corporation. AMD and Athlon and trademarks of Advanced Micro Devices, Inc.
Red-Black Successive Over-Relaxation (SOR) is a method of solving partial differential equations. In the parallel version, the program divides the red and the black array into roughly equal size bands of rows, assigning each band to a different processor. Communication occurs across the boundary rows between bands. In the TreadMarks version, the arrays are allocated in shared memory, and processors synchronize using barriers. With PVM, each processor explicitly sends the boundary rows to its neighbors
In numerical analysis, a multigrid method (MG method) is an algorithm for solving differential equations using a hierarchy of discretizations.
行波进位（Ripple Carry）与超前进位（Loodahead Carry)

## Slide 13: Course Objectives
Understand role & relationship of hardware and software
Exposure to （接触到）. . .
  Machine organization
  Assembly language programming
Understand how to build entire (slow) computing system
  Hardware and software
Be distinguished from mere programmers
    计算机系统（晶体管器件、数字逻辑、组成原理、高级语言的编译与汇编、高级语言的硬件实现、操作系统）核心概念和思想的最小集

## Slide 14: Course Objectives
“Any sufficiently advanced technology is indistinguishable from magic.”
Arthur C. Clarke, "Profiles of The Future” (Clarke's 3rd law)
No magic: Computers should NOT be magic to computer scientists!
Bottom UP: Start with what they “know” (I wish)
  Computing systems from transistors on up
  The transistor as light switch
Choose a computer model that is simple
  Not about “design”, but about “insight” into all computers
  As the genius said: simple, but still rich
  Continually build on what you know
  Continually raising the level of abstraction
  Memorizing as little as absolutely necessary
  Trying very hard to not introduce magic

## Slide 15: Courses Contents
Overview
Operations on bits, bytes (arithmetic, logical)
The transistor
Digital Logic
The finite state machine
The Von Neumann model
The LC-3 Instruction set architecture
Programming and Debugging
Assembly Language programming
Physical I/O
Subroutines, Calls, traps, interrupts
12. Transition to C
13. Programming in C

## Slide 16: Computational model (Turing machine) vs. Structural model (Von structure)
U
a,b,c
c(a+b)
Universal Turing Machine
Tadd, Tmul

## Slide 17: Computational model (Turing machine) vs. Structural model (Von structure)
U
a,b,c
c(a+b)
Universal Turing Machine
Tadd, Tmul

## Slide 18: Instruction Set Architecture (ISA) vs. Finite State Machine

## Slide 19: Instruction Set Architecture (ISA) vs. Finite State Machine

## Slide 20: Computer microarchitecture vs. Finite State Machine

## Slide 21: Levels of Abstraction
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 22: What’s this?
一座城市！

## Slide 23: N-type MOS Transistor
MOS = Metal Oxide Semiconductor 金属氧化物半导体
  two types: N-type and P-type
N-type
  when Gate has positive voltage, short circuit between #1 and #2 (switch closed)
  when Gate has zero voltage, open circuit between #1 and #2 (switch open)
Gate = 1
Gate = 0
Terminal #2 must be
connected to GND (0V).
抽象

## Slide 24: P-type MOS Transistor
P-type is complementary to N-type
  when Gate has positive voltage, open circuit between #1 and #2 (switch open)
  when Gate has zero voltage, short circuit between #1 and #2 (switch closed)
Gate = 1
Gate = 0
Terminal #1 must be
connected to +2.9V.

## Slide 25: Levels of Abstraction
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 26: Inverter (NOT Gate)
In | Out
0 V | 2.9 V
2.9 V | 0 V
In | Out
0 | 1
1 | 0
Truth table
2.9V
0V

## Slide 27: OR Gate
Add inverter to NOR.
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 28: AND Gate
Add inverter to NAND.
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 29: Gates

## Slide 30: Levels of Abstraction
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 31: Basic Logical Structure

## Slide 32: Levels of Abstraction
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 33
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
MEM.EN,R,W
16
MAR
16
LD.MAR
PC
GatePC
OUTPUT
MEMORY
MUX
MUX
MDR
…
+
16
16
16
16
ADDR1MUX
2
PCMUX
+1
16
MARMUX
SEXT
[7:0]
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
LD.MDR
MUX
MIO.EN
GateMDR
16
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
LC-3 Data Path(Microarchitecture)
Control Unit
Memory Unit
Processing Unit

## Slide 34: Levels of Abstraction
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 35: LC-3 ISA Overview
运算指令(Operate Instructions)
0
0
0
1
DR
SR1
0
0
0
SR2
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
0
0
0
1
DR
SR1
1
Imm5
0
1
0
1
DR
SR1
0
0
0
SR2
0
1
0
1
DR
SR1
1
Imm5
1
0
0
1
DR
SR1
1
1
1
1
1
1
1
1
0
1
ADD
AND
AND
NOT
Reserved
ADD
控制指令(Control Instructions)
1
1
1
1
0
0
0
0
TrapVector8
TRAP
0
0
0
0
n
z
p
PCoffset9
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
0
1
0
0
1
PCoffset11
0
1
0
0
0
0
0
BaseR
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
BR
JSRR
RTI
JSR
1
1
0
0
0
0
0
BaseR
0
0
0
0
0
0
JMP
1
1
0
0
0
0
0
1
1
1
0
0
0
0
0
0
RET
数据移动指令
(Data Movement Instructions)
0
0
1
0
DR
PCoffset9
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
0
1
1
0
DR
BaseR
PCoffset6
1
0
1
0
DR
PCoffset9
1
1
1
0
DR
PCoffset9
LD
LDI
LEA
LDR
0
0
1
1
SR
PCoffset9
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
0
1
1
1
SR
BaseR
PCoffset6
1
0
1
1
SR
PCoffset9
ST
STI
STR
取数指令(Load)
存数指令(Store)

## Slide 36: Outline
Course and Crew
1
What's the difference between “Big" and "Small"?
2
Why Take This Course?
3
Great Ideas in Computing Systems
4
What’s This Course All About ?
5
Summary
6

## Slide 37
Abstraction Layers in Modern Systems
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics
Application

## Slide 38: Acknowledgements
Special thanks to Prof. An
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
  Krste Asanovic (UCB)