## Slide 1: Chapter 3-2 Combinational Logic Circuits & Basic Storage Elements
计算机科学与技术学院
School of Computer Science and Technology
计算机系统概论
Introduction to Computing Systems
（ CS1002A.01 ）

## Slide 2
Outline
Review
1
3
Basic Storage Elements
2
Combinational Logic Circuits
4
Summary

## Slide 3
Outline
Review
1
3
Basic Storage Elements
2
Combinational Logic Circuits
4
Summary

## Slide 4: Review
Transistor: Building Block of Computers
  Logically, each transistor acts as a switch
Combined to implement logic functions
  AND, OR, NOT

## Slide 5: N-type MOS Transistor
MOS = Metal Oxide Semiconductor
  two types: N-type and P-type
N-type
  when Gate has positive voltage, short circuit between #1 and #2 (switch closed)
  when Gate has zero voltage, open circuit between #1 and #2 (switch open)
Gate = 1
Gate = 0
Terminal #2 must be
connected to GND (0V).
Notes: 5

## Slide 6: P-type MOS Transistor
P-type is complementary to N-type
  when Gate has positive voltage, open circuit between #1 and #2 (switch open)
  when Gate has zero voltage, short circuit between #1 and #2 (switch closed)
Gate = 1
Gate = 0
Terminal #1 must be
connected to +2.9V.
Notes: 6

## Slide 7: Gates

## Slide 8: Today: Building Functions from Logic Gates
We've already seen how to implement truth tables using AND, OR, and NOT -- an example of combinational logic.
Combinational Logic Circuit
  output depends only on the current inputs
  stateless
Sequential Logic Circuit
  output depends on the sequence of inputs (past and present)
  stores information (state) from past inputs
We'll first look at some useful combinational circuits, then show how to use sequential circuits to store information.

## Slide 9: Approach: Bottom Up
Transistor Physical Layout
Scheme for
Representing Information
Register Transfer Level (RTL) Design
1K~10K Cells/Module
(100K Devices)
ALU
Full Adder
Gate Level Design
Circuit Level Design
（Transistor Level Design）
(2~8 Devices/Gate)
Register Transfer Level (RTL) Design
2~16 Gates/Cell
(16~64 Devices)
Clk
Register
+
Cout
S
A
B
Cin
Integrated Circuit Design
100 Modules/ IC
0.25M~20G Devices
Now, You are Here.
And Here.

## Slide 10: Great Idea #3: Abstraction Helps Us Manage Complexity
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 11: Great Idea #4: Software and Hardware Co-design
Software
Hardware
Application
Language
Machine Architecture, ISA
Microarchitecture
Logic and IC
Device
Algorithm & Data Structure
Computer System: Layers of Abstraction
Now, You are Here.
Notes: 11

## Slide 12
Outline
Review
1
3
Basic Storage Elements
2
Combinational Logic Circuits
4
Summary

## Slide 13: Decoder
n inputs, 2n outputs
  exactly one output is 1 for each possible input pattern
2-bit
decoder
Notes: 13
Uses of decoder:
convert memory/register address to a control line that selects that location
convert an opcode to one of n control lines

## Slide 14: Decoder
n inputs, 2n outputs
  exactly one output is 1 for each possible input pattern
2-bit
decoder
How many transistors?
Notes: 14
Uses of decoder:
convert memory/register address to a control line that selects that location
convert an opcode to one of n control lines

## Slide 15: Multiplexer (MUX)
n-bit selector and 2n inputs, one output
  output equals one of the inputs, depending on selector
4-to-1 MUX
Notes: 15
Another view: decode S, and AND each output with one of the MUX inputs.
Also explain multi-bit inputs.
Uses of multiplexer:
select which input to use for function
select which computed value to pass to next stage (or to place on bus)

## Slide 16: Full Adder
Add two bits and carry-in, produce one-bit sum and carry-out.
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: 16
A half-adder is one that doesn't take a carry-in.
Sum is one when 1 or 3 inputs are one. Carry-out is one when 2 or 3 inputs are one.

## Slide 17: Four-bit Adder
Notes: 17
This is called a "ripple-carry" adder. The sum becomes valid as the carry ripples its way from the low bit to the high bit. How many gate delays until the output is settled?

## Slide 18: Adder/Subtracter - Approach #1
A+B
A-B

## Slide 19: Adder/Subtracter - Approach #2

## Slide 20: Incrementor
Let’s create an incrementor
  Input: A (as a 16-bit 2’s complement integer)
  Output: A+1 (also as a 16-bit 2’s complement integer)
Approach #1 (impractical):
  Use PLA-like techniques to implement circuit
  Problem: 216 or 65536 rows, 16 output columns
  In theory, possible; in practice, intractable
Approach#2 (pragmatic):
  Create a 1-bit incrementor circuit
  Replicate it 16 times

## Slide 21: One-bit Incrementor
Implement a single-column of an incrementor
A | Cin | S | Cout
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 22
Outline
Review
1
3
Basic Storage Elements
2
Combinational Logic Circuits
4
Summary

## Slide 23: Combinational vs. Sequential
Combinational Circuit
  always gives the same output for a given set of inputs
    ex: adder always generates sum and carry, regardless of previous inputs
Sequential Circuit
  stores information
  output depends on stored information (state) plus input
    so a given input might produce different outputs, depending on the stored information
  example: ticket counter
    advances when you push the button
    output depends on previous state
  useful for building “memory” elements and “state machines”
Notes: 23

## Slide 24: R-S Latch: Simple Storage Element
R is used to “reset” or “clear” the element – set it to zero.
S is used to “set” the element – set it to one.
If both R and S are 1, out could be either 1 or 0.
  “quiescent” state -- holds its previous value
  note: if a is 1, b is 0, and vice versa
1
0
1
1
1
1
0
0
1
1
0
0
1
1

## Slide 25: Clearing the R-S latch
Suppose we start with output = 1, then change R to 0.
Output changes to zero.
Then set R=1 to “store” value in quiescent state.
1
0
1
1
1
1
0
0
1
0
1
0
0
0
1
1
Notes: 25
Setting R to zero forces b (and B) to 1, which forces a (and A) to zero.
This is a stable state, because R=0 and A=0 means b=1.
Bring R back to one then keeps the output at zero.
What is the result if we start with a=0?

## Slide 26: Setting the R-S Latch
Suppose we start with output = 0, then change S to 0.
Output changes to one.
Then set S=1 to “store” value in quiescent state.
1
1
0
0
1
1
0
1
1
1
0
0
Notes: 26
Setting S to zero forces a (and A) to 1, which forces b (and B) to zero.
This is a stable state, because S=0 and B=0 means a=1.
Bring S back to one then keeps the output at one.
What is the result if we start with a=1?

## Slide 27: R-S Latch Summary
R = S = 1
  hold current value in latch
S =1 and R => 0,
  set value to 0
R=1 and S => 0
  set value to 1
R = S = 0
  both outputs equal 1
  final state determined by electrical properties of gates
  Don’t do it!

## Slide 28: Gated D-Latch
Two inputs: D (data) and WE (Write Enable)
  when WE = 1, latch is set to value of D
    S = NOT(D), R = D
  when WE = 0, latch holds previous value
    S = R = 1
Notes: 28
The D-latch is used to store a single data bit. The latch is set to the value of D whenever WE=1; when WE=0, the current value is stored, no matter what D becomes.
Using D and not(D) to control S and R makes it easier to ensure that S and R are never zero at the same time.
WE allows us to control when a new value is written to the latch.

## Slide 29: Register
A register stores a multi-bit value.
  We use a collection of D-latches, all controlled by a common WE.
  When WE=1, n-bit value D is written to register.

## Slide 30: Representing Multi-bit Values
Number bits from right (0) to left (n-1)
  just a convention -- could be left to right, but must be consistent
Use brackets [] to denote range: D[l:r] denotes bit l to bit r, from left to right
May also see A<14:9>, especially in hardware block diagrams.
A = 0101001101010101
A[2:0] = 101
A[14:9] = 101001
0
15

## Slide 31: Memory
Now that we know how to store bits, we can build a memory – a logical k × m array of stored bits.
•
•
•
k = 2n
locations
m bits
Address Space:
number of locations (usually a power of 2)
Addressability:
number of bits per location (e.g., byte-addressable)

## Slide 32: 22 x 3 Memory
address
decoder
word select
word WE
address
write
enable
input bits
output bits
Notes: 32
Decoder asserts one of the word select lines, based on address.
Word select activates one of the output AND gates, which drives the selected data to the output OR gate. (For a read, this is basically a MUX -- decoder ANDed with signals, results ORed together.)
When writing, the only WE bits for the proper word are asserted (based on decoder again).

## Slide 33: More Memory Details
This is a not the way actual memory is implemented.
  fewer transistors, much more dense, relies on electrical properties
But the logical structure is very similar.
  address decoder
  word select line
  word write enable
Two basic kinds of RAM (Random Access Memory)
  Static RAM (SRAM)
    fast, not very dense (bitcell is a latch)
  Dynamic RAM (DRAM)
    slower but denser, bit storage must be periodically refreshed
    each bitcell is a capacitor (like a leaky bucket) that decays
Also, non-volatile memories: ROM, PROM, flash, …

## Slide 34: SRAM Memory
n
D
D
D
. . .
D
D
D
. . .
D
D
D
. . .
. . .
m
Memory Data Out
m
Memory Data In
Read Address Decoder
Memory Read Address
n
Write Address Decoder
Memory WriteAddress
Gated
D-latch
D
Q
WE
Read bitlines
Write bitlines
Write word line
Read word line
. . .
. . .
WE

## Slide 35
Outline
Review
1
3
Basic Storage Elements
2
Combinational Logic Circuits
4
Summary

## Slide 36: Basic Logical Structure