## Slide 1: Chapter 16 Pointers and Arrays
陈俊仕
cjuns@ustc.edu.cn 2024 Fall
计算机科学与技术学院
School of Computer Science and Technology
计算系统概论A
Introduction to Computing Systems
（ CS1002A.03 ）

## Slide 2
Outline
Review
1
2
From ENIAC to the Stored Program Computer
Review
1
2
Pointers
2
From ENIAC to the Stored Program Computer
3
Arrays
2
From ENIAC to the Stored Program Computer
4
Summary

## Slide 3
Outline
Review
1
2
From ENIAC to the Stored Program Computer
Review
1
Pointers
2
From ENIAC to the Stored Program Computer
Arrays
2
From ENIAC to the Stored Program Computer
Summary

## Slide 4: Memory Model in the LC-3
PC
R4(Global pointer)
R6 (stack pointer)
Device Register
Addresses
0x0000
0xFFFF
Trap Vector Table
Interrupt Vector Table
Operating System
and Supervisor Stack
0x00FF
0x0100
0x01FF
0x0200
0x2FFF
0x3000
0xFDFF
0xFE00
Run-time stack
Program Text
Global data section
Heap (for dynamically
allocated memory)
R5 (frame pointer)
R5
Function2
R6
R5
R6
Function3
Function1
R5
R6

## Slide 5: Run-Time Stack
1 int main(void)
2 {
3 int a;
4 int b;
5
6 b = Watt(a); // main calls Watt first
7 b = Volt(a, b); // then calls Volt
8 }
9
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10); // Watt calls Volt
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }

## Slide 6: Run-time stack when execution starts
1 int main(void)
2 {
3 int a;
4 int b;
5
6 b = Watt(a); // main calls Watt first
7 b = Volt(a, b); // then calls Volt
8 }
9
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10); // Watt calls Volt
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
main
Memory
x0000
xFFFF
R5
R6

## Slide 7: Run-time stack when Watt executes
1 int main(void)
2 {
3 int a;
4 int b;
5
6 b = Watt(a); // main calls Watt first
7 b = Volt(a, b); // then calls Volt
8 }
9
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10); // Watt calls Volt
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
main
Memory
x0000
xFFFF
R5
R6
Watt

## Slide 8: Run-time stack when Volt executes
1 int main(void)
2 {
3 int a;
4 int b;
5
6 b = Watt(a); // main calls Watt first
7 b = Volt(a, b); // then calls Volt
8 }
9
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10); // Watt calls Volt
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
main
Memory
x0000
xFFFF
R5
R6
Watt
Volt

## Slide 9: Run-time stack after Volt completes
1 int main(void)
2 {
3 int a;
4 int b;
5
6 b = Watt(a); // main calls Watt first
7 b = Volt(a, b); // then calls Volt
8 }
9
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10); // Watt calls Volt
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
main
Memory
x0000
xFFFF
R5
R6
Watt

## Slide 10: Run-time stack after Watt completes
1 int main(void)
2 {
3 int a;
4 int b;
5
6 b = Watt(a); // main calls Watt first
7 b = Volt(a, b); // then calls Volt
8 }
9
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10); // Watt calls Volt
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
main
Memory
x0000
xFFFF
R5
R6

## Slide 11: Run-time stack when Volt executes
1 int main(void)
2 {
3 int a;
4 int b;
5
6 b = Watt(a); // main calls Watt first
7 b = Volt(a, b); // then calls Volt
8 }
9
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10); // Watt calls Volt
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
main
Memory
x0000
xFFFF
R5
R6
Volt

## Slide 12: Run-time stack after Volt completes
1 int main(void)
2 {
3 int a;
4 int b;
5
6 b = Watt(a); // main calls Watt first
7 b = Volt(a, b); // then calls Volt
8 }
9
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10); // Watt calls Volt
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
main
Memory
x0000
xFFFF
R5
R6

## Slide 13: Function call in C
Four steps of the C-runtime stack protocol
  The caller copies arguments for the callee onto the run-time stack and passes control to the callee
  The callee function pushes space for local variables and other info. onto the run-time stack, creating its stack frame on top of the stack
  The callee executes the task
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller

## Slide 14: Function call in C
Four steps of the C-runtime stack protocol
  The caller copies arguments for the callee onto the run-time stack and passes control to the callee
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
AND R0,R0,#0 ; R0 <- 0
ADD R0,R0,#10 ; R0 <- 10
ADD R6,R6,#-1 ;
STR R0,R6,#0 ; Push 10 onto stack
LDR R0,R5,#0 ; Load w
ADD R6,R6,#-1 ;
STR R0,R6,#0 ; Push w
JSR Volt
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt

## Slide 15: Function call in C
Four steps of the C-runtime stack protocol
  The caller copies arguments for the callee onto the run-time stack and passes control to the callee
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
AND R0,R0,#0 ; R0 <- 0
ADD R0,R0,#10 ; R0 <- 10
ADD R6,R6,#-1 ;
STR R0,R6,#0 ; Push 10 onto stack
LDR R0,R5,#0 ; Load w
ADD R6,R6,#-1 ;
STR R0,R6,#0 ; Push w
JSR Volt
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
Parameters
for Watt

## Slide 16: Function call in C
Four steps of the C-runtime stack protocol
  The caller copies arguments for the callee onto the run-time stack and passes control to the callee
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
AND R0,R0,#0 ; R0 <- 0
ADD R0,R0,#10 ; R0 <- 10
ADD R6,R6,#-1 ;
STR R0,R6,#0 ; Push 10 onto stack
LDR R0,R5,#0 ; Load w
ADD R6,R6,#-1 ;
STR R0,R6,#0 ; Push w
JSR Volt
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
Parameters
for Watt
value of w

## Slide 17: Function call in C
Four steps of the C-runtime stack protocol
  The caller copies arguments for the callee onto the run-time stack and passes control to the callee
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
AND R0,R0,#0 ; R0 <- 0
ADD R0,R0,#10 ; R0 <- 10
ADD R6,R6,#-1 ;
STR R0,R6,#0 ; Push 10 onto stack
LDR R0,R5,#0 ; Load w
ADD R6,R6,#-1 ;
STR R0,R6,#0 ; Push w
JSR Volt
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
Parameters
for Watt
value of w

## Slide 18: Function call in C
Four steps of the C-runtime stack protocol
  The callee function pushes space for local variables and other info. onto the run-time stack, creating its stack frame on top of the stack
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
18
19 int Volt(int q, int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
Volt:
ADD R6,R6,#-1 ; alloc. spot for the
; return value
ADD R6,R6,#-1 ;
STR R7,R6,#0 ; push R7 (return addr.)
ADD R6,R6,#-1
STR R5,R6,#0 ; push R5
; (caller's frame pointer)
ADD R5,R6,#-1 ; set frame pointer for Volt
ADD R6,R6,#-2 ; alloc. memory for
; Volt's local variables
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
Parameters
for Watt
value of w

## Slide 19: Function call in C
Four steps of the C-runtime stack protocol
  The callee function pushes space for local variables and other info. onto the run-time stack, creating its stack frame on top of the stack
18
19 int Volt(int q, int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
Volt:
ADD R6,R6,#-1 ; alloc. spot for the
; return value
ADD R6,R6,#-1 ;
STR R7,R6,#0 ; push R7 (return addr.)
ADD R6,R6,#-1
STR R5,R6,#0 ; push R5
; (caller's frame pointer)
ADD R5,R6,#-1 ; set frame pointer for Volt
ADD R6,R6,#-2 ; alloc. memory for
; Volt's local variables
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
Parameters
for Watt
value of w
Stack frame
of Volt

## Slide 20: Function call in C
Four steps of the C-runtime stack protocol
  The callee function pushes space for local variables and other info. onto the run-time stack, creating its stack frame on top of the stack
18
19 int Volt(int q, int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
Volt:
ADD R6,R6,#-1 ; alloc. spot for the
; return value
ADD R6,R6,#-1 ;
STR R7,R6,#0 ; push R7 (return addr.)
ADD R6,R6,#-1
STR R5,R6,#0 ; push R5
; (caller's frame pointer)
ADD R5,R6,#-1 ; set frame pointer for Volt
ADD R6,R6,#-2 ; alloc. memory for
; Volt's local variables
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
Parameters
for Watt
value of w
Ret. value to Watt
Stack frame
of Volt
Bookkeeping
info

## Slide 21: Function call in C
Four steps of the C-runtime stack protocol
  The callee function pushes space for local variables and other info. onto the run-time stack, creating its stack frame on top of the stack
18
19 int Volt(int q, int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
Volt:
ADD R6,R6,#-1 ; alloc. spot for the
; return value
ADD R6,R6,#-1 ;
STR R7,R6,#0 ; push R7 (return addr.)
ADD R6,R6,#-1
STR R5,R6,#0 ; push R5
; (caller's frame pointer)
ADD R5,R6,#-1 ; set frame pointer for Volt
ADD R6,R6,#-2 ; alloc. memory for
; Volt's local variables
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
Parameters
for Watt
value of w
Ret. value to Watt
Ret. addr. for Watt
Stack frame
of Volt
Bookkeeping
info

## Slide 22: Function call in C
Four steps of the C-runtime stack protocol
  The callee function pushes space for local variables and other info. onto the run-time stack, creating its stack frame on top of the stack
18
19 int Volt(int q, int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
Volt:
ADD R6,R6,#-1 ; alloc. spot for the
; return value
ADD R6,R6,#-1 ;
STR R7,R6,#0 ; push R7 (return addr.)
ADD R6,R6,#-1
STR R5,R6,#0 ; push R5
; (caller's frame pointer)
ADD R5,R6,#-1 ; set frame pointer for Volt
ADD R6,R6,#-2 ; alloc. memory for
; Volt's local variables
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info

## Slide 23: Function call in C
Four steps of the C-runtime stack protocol
  The callee function pushes space for local variables and other info. onto the run-time stack, creating its stack frame on top of the stack
18
19 int Volt(int q, int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
Volt:
ADD R6,R6,#-1 ; alloc. spot for the
; return value
ADD R6,R6,#-1 ;
STR R7,R6,#0 ; push R7 (return addr.)
ADD R6,R6,#-1
STR R5,R6,#0 ; push R5
; (caller's frame pointer)
ADD R5,R6,#-1 ; set frame pointer for Volt
ADD R6,R6,#-2 ; alloc. memory for
; Volt's local variables
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
Local variables

## Slide 24: Function call in C
Four steps of the C-runtime stack protocol
  The callee function pushes space for local variables and other info. onto the run-time stack, creating its stack frame on top of the stack
18
19 int Volt(int q, int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
Volt:
ADD R6,R6,#-1 ; alloc. spot for the
; return value
ADD R6,R6,#-1 ;
STR R7,R6,#0 ; push R7 (return addr.)
ADD R6,R6,#-1
STR R5,R6,#0 ; push R5
; (caller's frame pointer)
ADD R5,R6,#-1 ; set frame pointer for Volt
ADD R6,R6,#-2 ; alloc. memory for
; Volt's local variables
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 25: Function call in C
Four steps of the C-runtime stack protocol
  The callee executes the task
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
18
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }

## Slide 26: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
LDR R0,R5,#0 ; Load local variable k
STR R0,R5,#3 ; Write it in return value slot, which
; will always be at location R5 + 3
ADD R6,R5,#1 ; Pop local variables
LDR R5,R6,#0 ; Pop the frame pointer
ADD R6,R6,#1 ;
LDR R7,R6,#0 ; Pop the return address
ADD R6,R6,#1 ;
RET
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 27: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
LDR R0,R5,#0 ; Load local variable k
STR R0,R5,#3 ; Write it in return value slot, which
; will always be at location R5 + 3
ADD R6,R5,#1 ; Pop local variables
LDR R5,R6,#0 ; Pop the frame pointer
ADD R6,R6,#1 ;
LDR R7,R6,#0 ; Pop the return address
ADD R6,R6,#1 ;
RET
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 28: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
LDR R0,R5,#0 ; Load local variable k
STR R0,R5,#3 ; Write it in return value slot, which
; will always be at location R5 + 3
ADD R6,R5,#1 ; Pop local variables
LDR R5,R6,#0 ; Pop the frame pointer
ADD R6,R6,#1 ;
LDR R7,R6,#0 ; Pop the return address
ADD R6,R6,#1 ;
RET
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 29: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
LDR R0,R5,#0 ; Load local variable k
STR R0,R5,#3 ; Write it in return value slot, which
; will always be at location R5 + 3
ADD R6,R5,#1 ; Pop local variables
LDR R5,R6,#0 ; Pop the frame pointer
ADD R6,R6,#1 ;
LDR R7,R6,#0 ; Pop the return address
ADD R6,R6,#1 ;
RET
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 30: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
LDR R0,R5,#0 ; Load local variable k
STR R0,R5,#3 ; Write it in return value slot, which
; will always be at location R5 + 3
ADD R6,R5,#1 ; Pop local variables
LDR R5,R6,#0 ; Pop the frame pointer
ADD R6,R6,#1 ;
LDR R7,R6,#0 ; Pop the return address
ADD R6,R6,#1 ;
RET
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 31: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
LDR R0,R5,#0 ; Load local variable k
STR R0,R5,#3 ; Write it in return value slot, which
; will always be at location R5 + 3
ADD R6,R5,#1 ; Pop local variables
LDR R5,R6,#0 ; Pop the frame pointer
ADD R6,R6,#1 ;
LDR R7,R6,#0 ; Pop the return address
ADD R6,R6,#1 ;
RET
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 32: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
LDR R0,R5,#0 ; Load local variable k
STR R0,R5,#3 ; Write it in return value slot, which
; will always be at location R5 + 3
ADD R6,R5,#1 ; Pop local variables
LDR R5,R6,#0 ; Pop the frame pointer
ADD R6,R6,#1 ;
LDR R7,R6,#0 ; Pop the return address
ADD R6,R6,#1 ;
RET
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 33: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
19 int Volt(int q; int r)
20 {
21 int k;
22 int m;
23
24 return k;
25 }
LDR R0,R5,#0 ; Load local variable k
STR R0,R5,#3 ; Write it in return value slot, which
; will always be at location R5 + 3
ADD R6,R5,#1 ; Pop local variables
LDR R5,R6,#0 ; Pop the frame pointer
ADD R6,R6,#1 ;
LDR R7,R6,#0 ; Pop the return address
ADD R6,R6,#1 ;
RET
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 34: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
JSR Volt
LDR R0,R6,#0 ; Load the return value
STR R0,R5,#0 ; w = Volt(w, 10);
ADD R6,R6,#1 ; Pop return value
ADD R6,R6,#2 ; Pop arguments
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 35: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
JSR Volt
LDR R0,R6,#0 ; Load the return value
STR R0,R5,#0 ; w = Volt(w, 10);
ADD R6,R6,#1 ; Pop return value
ADD R6,R6,#2 ; Pop arguments
w
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 36: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
JSR Volt
LDR R0,R6,#0 ; Load the return value
STR R0,R5,#0 ; w = Volt(w, 10);
ADD R6,R6,#1 ; Pop return value
ADD R6,R6,#2 ; Pop arguments
w (k)
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 37: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
JSR Volt
LDR R0,R6,#0 ; Load the return value
STR R0,R5,#0 ; w = Volt(w, 10);
ADD R6,R6,#1 ; Pop return value
ADD R6,R6,#2 ; Pop arguments
w (k)
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 38: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
JSR Volt
LDR R0,R6,#0 ; Load the return value
STR R0,R5,#0 ; w = Volt(w, 10);
ADD R6,R6,#1 ; Pop return value
ADD R6,R6,#2 ; Pop arguments
w (k)
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt
10
value of w
Ret. value to Watt (k)
Ret. addr. for Watt
Stack frame
of Volt
Watt’s frame pointer
Parameters
for Watt
Bookkeeping
info
k
m
Local variables

## Slide 39: Function call in C
Four steps of the C-runtime stack protocol
  Once it is ready to return, the callee removes, or pops, its stack frame oﬀ the run-time stack and returns the return value and control to the caller
10 int Watt(int a)
11 {
12 int w;
13
14 w = Volt(w, 10);
15
16 return w;
17 }
JSR Volt
LDR R0,R6,#0 ; Load the return value
STR R0,R5,#0 ; w = Volt(w, 10);
ADD R6,R6,#1 ; Pop return value
ADD R6,R6,#2 ; Pop arguments
w (k)
Local variable
of Watt
R6
R5
x0000
xFFFF
Stack frame
of Watt

## Slide 40
Outline
Review
1
2
From ENIAC to the Stored Program Computer
Review
2
Pointers
3
4
From ENIAC to the Stored Program Computer
Summary
Arrays

## Slide 41: A classic example --‘Swap’
1 #include <stdio.h>
2
3 // Swap has no return value thus is declared as void
4 void Swap(int firstVal, int secondVal);
5
6 int main(void)
7 {
8 int valueA = 3;
9 int valueB = 4;
10
11 printf("Before Swap ");
12 printf("valueA = %d and valueB = %d\n", valueA, valueB);
13
14 Swap(valueA, valueB);
15
16 printf("After Swap ");
17 printf("valueA = %d and valueB = %d\n", valueA, valueB);
18 }
19
20 void Swap(int firstVal, int secondVal)
21 {
22 int tempVal; // Holds firstVal when swapping
23
24 tempVal = firstVal;
25 firstVal = secondVal;
26 secondVal = tempVal;
27 }
Run-time stack
4
3
valueB
valueA
R6
R5
x0000
xFFFF
Stack frame
for main

## Slide 42: A classic example --‘Swap’
1 #include <stdio.h>
2
3 // Swap has no return value thus is declared as void
4 void Swap(int firstVal, int secondVal);
5
6 int main(void)
7 {
8 int valueA = 3;
9 int valueB = 4;
10
11 printf("Before Swap ");
12 printf("valueA = %d and valueB = %d\n", valueA, valueB);
13
14 Swap(valueA, valueB);
15
16 printf("After Swap ");
17 printf("valueA = %d and valueB = %d\n", valueA, valueB);
18 }
19
20 void Swap(int firstVal, int secondVal)
21 {
22 int tempVal; // Holds firstVal when swapping
23
24 tempVal = firstVal;
25 firstVal = secondVal;
26 secondVal = tempVal;
27 }
main’s frame pointer
Return address in main
Return value to main
3
4
Run-time stack
4
3
valueB
valueA
secondVal
firstVal
tempVal
R6
R5
x0000
xFFFF
Stack frame
for Swap
Stack frame
for main

## Slide 43: A classic example --‘Swap’
1 #include <stdio.h>
2
3 // Swap has no return value thus is declared as void
4 void Swap(int firstVal, int secondVal);
5
6 int main(void)
7 {
8 int valueA = 3;
9 int valueB = 4;
10
11 printf("Before Swap ");
12 printf("valueA = %d and valueB = %d\n", valueA, valueB);
13
14 Swap(valueA, valueB);
15
16 printf("After Swap ");
17 printf("valueA = %d and valueB = %d\n", valueA, valueB);
18 }
19
20 void Swap(int firstVal, int secondVal)
21 {
22 int tempVal; // Holds firstVal when swapping
23
24 tempVal = firstVal;
25 firstVal = secondVal;
26 secondVal = tempVal;
27 }
main’s frame pointer
Return address in main
Return value to main
3
4
Run-time stack
4
3
valueB
valueA
secondVal
firstVal
tempVal
3
R6
R5
x0000
xFFFF
Stack frame
for Swap
Stack frame
for main

## Slide 44: A classic example --‘Swap’
1 #include <stdio.h>
2
3 // Swap has no return value thus is declared as void
4 void Swap(int firstVal, int secondVal);
5
6 int main(void)
7 {
8 int valueA = 3;
9 int valueB = 4;
10
11 printf("Before Swap ");
12 printf("valueA = %d and valueB = %d\n", valueA, valueB);
13
14 Swap(valueA, valueB);
15
16 printf("After Swap ");
17 printf("valueA = %d and valueB = %d\n", valueA, valueB);
18 }
19
20 void Swap(int firstVal, int secondVal)
21 {
22 int tempVal; // Holds firstVal when swapping
23
24 tempVal = firstVal;
25 firstVal = secondVal;
26 secondVal = tempVal;
27 }
main’s frame pointer
Return address in main
Return value to main
4
4
Run-time stack
4
3
valueB
valueA
secondVal
firstVal
tempVal
3
R6
R5
x0000
xFFFF
Stack frame
for Swap
Stack frame
for main

## Slide 45: A classic example --‘Swap’
1 #include <stdio.h>
2
3 // Swap has no return value thus is declared as void
4 void Swap(int firstVal, int secondVal);
5
6 int main(void)
7 {
8 int valueA = 3;
9 int valueB = 4;
10
11 printf("Before Swap ");
12 printf("valueA = %d and valueB = %d\n", valueA, valueB);
13
14 Swap(valueA, valueB);
15
16 printf("After Swap ");
17 printf("valueA = %d and valueB = %d\n", valueA, valueB);
18 }
19
20 void Swap(int firstVal, int secondVal)
21 {
22 int tempVal; // Holds firstVal when swapping
23
24 tempVal = firstVal;
25 firstVal = secondVal;
26 secondVal = tempVal;
27 }
main’s frame pointer
Return address in main
Return value to main
4
3
Run-time stack
4
3
valueB
valueA
secondVal
firstVal
tempVal
3
R6
R5
x0000
xFFFF
Stack frame
for Swap
Stack frame
for main

## Slide 46: A classic example --‘Swap’
1 #include <stdio.h>
2
3 // Swap has no return value thus is declared as void
4 void Swap(int firstVal, int secondVal);
5
6 int main(void)
7 {
8 int valueA = 3;
9 int valueB = 4;
10
11 printf("Before Swap ");
12 printf("valueA = %d and valueB = %d\n", valueA, valueB);
13
14 Swap(valueA, valueB);
15
16 printf("After Swap ");
17 printf("valueA = %d and valueB = %d\n", valueA, valueB);
18 }
19
20 void Swap(int firstVal, int secondVal)
21 {
22 int tempVal; // Holds firstVal when swapping
23
24 tempVal = firstVal;
25 firstVal = secondVal;
26 secondVal = tempVal;
27 }
main’s frame pointer
Return address in main
Return value to main
4
3
Run-time stack
4
3
valueB
valueA
secondVal
firstVal
tempVal
3
R6
R5
x0000
xFFFF
Stack frame
for Swap
Stack frame
for main

## Slide 47: Pointers
Declaring Pointer Variables
  point to the variable whose address it contains
  Example:
    int *ptr;
    char *cp;
    double *dp;
C has two pointer-related operators
  Address operator: &
  Indirection/dereference operator: *

## Slide 48: Pointer Operators (&)
The address operator: &
  Generates the memory address of its operand
  Example:
int object;
int *ptr;
object = 4;
ptr = &object;
AND R0,R0,#0 ; Clear R0
ADD R0,R0,#4 ; R0 = 4
STR R0,R5,#0 ; object = 4;
ADD R0,R5,#0 ; Generate memory
; address of object
STR R0,R5,#-1 ; Ptr = &object;

## Slide 49: Pointer Operators (*)
The indirection/dereference operator: *
  Indirectly manipulate the value of a memory object
  Example:
int object;
int *ptr;
object = 4;
ptr = &object;
*ptr = *ptr + 1;
LDR R0,R5,#-1 ; R0 contains the
; value of ptr
LDR R1,R0,#0 ; R1 <- *ptr
ADD R1,R1,#1 ; *ptr + 1
STR R1,R0,#0 ; *ptr = *ptr + 1;
-> 5
=> object = object + 1;

## Slide 50: Passing a Reference Using Pointers
1 #include <stdio.h>
2
3 void NewSwap(int firstVal, int secondVal);
4
5 int main(void)
6 {
7 int valueA = 3;
8 int valueB = 4;
9
10 printf("Before Swap ");
11 printf("valueA = %d and valueB = %d\n", valueA, valueB);
12
13 NewSwap(&valueA, &valueB);
14
15 printf("After Swap ");
16 printf("valueA = %d and valueB = %d\n", valueA, valueB);
17 }
18
19 void NewSwap(int *firstVal, int *secondVal)
20 {
21 int tempVal; // Holds firstVal when swapping
22
23 tempVal = *firstVal;
24 *firstVal = *secondVal;
25 *secondVal = tempVal;
26 }
main’s frame pointer
Return address in main
Return value to main
xEFFA
xEFF9
xEFF9
xEFF8
Run-time stack
4
3
valueB
valueA
secondVal
firstVal
tempVal
xEFF3
xEFF4
xEFF5
xEFF6
xEFF8
xEFFA

## Slide 51: Passing a Reference Using Pointers
1 #include <stdio.h>
2
3 void NewSwap(int firstVal, int secondVal);
4
5 int main(void)
6 {
7 int valueA = 3;
8 int valueB = 4;
9
10 printf("Before Swap ");
11 printf("valueA = %d and valueB = %d\n", valueA, valueB);
12
13 NewSwap(&valueA, &valueB);
14
15 printf("After Swap ");
16 printf("valueA = %d and valueB = %d\n", valueA, valueB);
17 }
18
19 void NewSwap(int *firstVal, int *secondVal)
20 {
21 int tempVal; // Holds firstVal when swapping
22
23 tempVal = *firstVal;
24 *firstVal = *secondVal;
25 *secondVal = tempVal;
26 }
main’s frame pointer
Return address in main
Return value to main
xEFFA
xEFF9
xEFF9
xEFF8
Run-time stack
4
3
valueB
valueA
secondVal
firstVal
tempVal
3
xEFF3
xEFF4
xEFF5
xEFF6
xEFF8
xEFFA

## Slide 52: Passing a Reference Using Pointers
1 #include <stdio.h>
2
3 void NewSwap(int firstVal, int secondVal);
4
5 int main(void)
6 {
7 int valueA = 3;
8 int valueB = 4;
9
10 printf("Before Swap ");
11 printf("valueA = %d and valueB = %d\n", valueA, valueB);
12
13 NewSwap(&valueA, &valueB);
14
15 printf("After Swap ");
16 printf("valueA = %d and valueB = %d\n", valueA, valueB);
17 }
18
19 void NewSwap(int *firstVal, int *secondVal)
20 {
21 int tempVal; // Holds firstVal when swapping
22
23 tempVal = *firstVal;
24 *firstVal = *secondVal;
25 *secondVal = tempVal;
26 }
main’s frame pointer
Return address in main
Return value to main
xEFFA
xEFF9
xEFF9
xEFF8
Run-time stack
4
4
valueB
valueA
secondVal
firstVal
tempVal
3
xEFF3
xEFF4
xEFF5
xEFF6
xEFF8
xEFFA

## Slide 53: Passing a Reference Using Pointers
1 #include <stdio.h>
2
3 void NewSwap(int firstVal, int secondVal);
4
5 int main(void)
6 {
7 int valueA = 3;
8 int valueB = 4;
9
10 printf("Before Swap ");
11 printf("valueA = %d and valueB = %d\n", valueA, valueB);
12
13 NewSwap(&valueA, &valueB);
14
15 printf("After Swap ");
16 printf("valueA = %d and valueB = %d\n", valueA, valueB);
17 }
18
19 void NewSwap(int *firstVal, int *secondVal)
20 {
21 int tempVal; // Holds firstVal when swapping
22
23 tempVal = *firstVal;
24 *firstVal = *secondVal;
25 *secondVal = tempVal;
26 }
main’s frame pointer
Return address in main
Return value to main
xEFFA
xEFF9
xEFF9
xEFF8
Run-time stack
3
4
valueB
valueA
secondVal
firstVal
tempVal
3
xEFF3
xEFF4
xEFF5
xEFF6
xEFF8
xEFFA

## Slide 54
Outline
Review
1
2
From ENIAC to the Stored Program Computer
Review
Pointers
3
4
From ENIAC to the Stored Program Computer
Summary
Arrays
3

## Slide 55: Arrays
Declaring Arrays
  Contiguous sequence of values
  Example:
    int grid[10];
  grid allocated in memory
    grid[0]…grid[9]

## Slide 56: Using Arrays – Example 1
The power of arrays comes from
  compute an array index using a C integral expression
Example 1:
  grid[6] = grid[3] + 1;
ADD R0,R5,#-9 ; Put the base address
; of grid into R0
LDR R1,R0,#3 ; R1 <-- grid[3]
ADD R1,R1,#1 ; R1 <-- grid[3] + 1
STR R1,R0,#6 ; grid[6] = grid[3] + 1;
R5 

## Slide 57: Using Arrays – Example 2
Example 2:
  grid[x+1] = grid[x] + 2;
LDR R0,R5,#-10 ; Load the value of x
ADD R1,R5,#-9 ; Put the base address
; of grid into R1
ADD R1,R0,R1 ; Calc. addr. of grid[x]
LDR R2,R1,#0 ; R2 <-- grid[x]
ADD R2,R2,#2 ; R2 <-- grid[x] + 2
LDR R0,R5,#-10 ; Load the value of x
ADD R0,R0,#1 ; R0 <-- x + 1
ADD R1,R5,#-9 ; Put the base address
; of grid into R1
ADD R1,R0,R1 ; Calc. addr. of grid[x+1]
STR R2,R1,#0 ; grid[x+1] = grid[x] + 2;
R5 
x

## Slide 58: Arrays as parameters
Passing arrays between functions
  option 1: pass the entire array of values
  option 2: pass a reference to the array
  If the array contains a large number of elements
    copying each element from one stack frame onto another could be very costly in execution time
  C naturally passes arrays by reference

## Slide 59: Arrays as parameters
Passing arrays between functions
  Example:
1 #include <stdio.h>
2 #define MAX_NUMS 10
3 int Average(int input_values[]);
4 int main(void)
5 {
6 int mean; // Average of numbers
7 int numbers[MAX_NUMS]; // Original input numbers
8
9 // Get input
// ...
16 mean = Average(numbers);
17 printf("The average of these numbers is %d\n", mean);
18 }
19
20 int Average(int inputValues[])
21 {
22 int sum = 0;
23 for (int index = 0; index < MAX_NUMS; index++) {
24 sum = sum + inputValues[index];
25 }
26 return (sum / MAX_NUMS);
27 }

## Slide 60: Arrays as parameters
1 #include <stdio.h>
2 #define MAX_NUMS 10
3 int Average(int input_values[]);
4 int main(void)
5 {
6 int mean; // Average of numbers
7 int numbers[MAX_NUMS]; // Original input numbers
8
9 // Get input
// ...
16 mean = Average(numbers);
17 printf("The average of these numbers is %d\n", mean);
18 }
19
20 int Average(int inputValues[])
21 {
22 int sum = 0;
23 for (int index = 0; index < MAX_NUMS; index++) {
24 sum = sum + inputValues[index];
25 }
26 return (sum / MAX_NUMS);
27 }

## Slide 61: Strings in C
Strings are sequences of characters that represent text
  Example:
    char word[10];
  Array word can contain the strings
    “elephant” or “giraﬀe”, but not the entirety of “hippopotamus”
  The null character – ‘\0’ (ASCII value: 0)
    Such strings are also called null-terminated strings.
char word[10];
word[0] = 'g';
word[1] = 'i';
word[2] = 'r';
word[3] = 'a';
word[4] = 'f';
word[5] = 'f';
word[6] = 'e';
word[7] = '\0';
printf("%s", word);
char word[10] = "Hello";
printf("%s", word);

## Slide 62: Arrays vs. Pointers in C
Example:
  Access the fourth character within the string
    word[3] or *(cptr + 3) or cptr[3]
  cptr is a variable and can be reassigned
  word is an array and cannot be reassigned
char word[10];
char *cptr;
cptr = word;

## Slide 63: Variable-Length Arrays
Arrays whose sizes are variable integer expressions, rather than constants (C99 standard)
  Example:
  The size of the array data can only be determined during execution of the code, and it is not known at compile time.
Array data is still allocated on the run-time stack
  requires additional instructions during allocation and access
More general solution:
  malloc/free, new[] / delete[]
int Calculate(int len)
{
int data[len];
// ...

## Slide 64
Outline
Review
1
2
From ENIAC to the Stored Program Computer
Review
Pointers
3
4
From ENIAC to the Stored Program Computer
Summary
Arrays
4

## Slide 65: Summary
Two programming constructs: Pointers and arrays
  Enable us to access memory indirectly
Pointers
  Variables that contain address of other memory objects
  Indirectly access and manipulate these other objects
    Pass parameters by reference
    Construct complex data structure
Arrays
  A collection of elements that the same type arranged sequentially in memory
  Access a particular element within an array by providing an index to the element that is its offset from the beginning of the array
  A significant structure for organizing data
    Character string, vector, tensor, stack, queue, …

## Slide 66: Exercise