## Slide 1: Chapter 9-1 Memory Mapped I/O
陈俊仕
cjuns@ustc.edu.cn 2024 Fall
计算机科学与技术学院
School of Computer Science and Technology
计算系统概论A
Introduction to Computing Systems
（ CS1002A.03 ）

## Slide 3
Outline
Review
1
2
From ENIAC to the Stored Program Computer
Review
1
2
The Memory Address Space
2
From ENIAC to the Stored Program Computer
3
Input/Output

## Slide 4: Review
So far, we’ve learned how to:
  compute with values in registers
  load data from memory to registers
  store data from registers to memory

## Slide 5: Today: I/O in Von Neumann Model

## Slide 6
Outline
Review
1
2
From ENIAC to the Stored Program Computer
Review
1
2
The Memory Address Space
2
From ENIAC to the Stored Program Computer
3
Input/Output

## Slide 7: Need for I/O
But where does data in memory come from? And how does data get out of the system so that humans can use it?
  Computer systems are useless unless they can process information from outside of the computer and output results outside of the computer
  I/O is effectively the communication with outside of the computer
I/O device itself communicates with outside world
  E.g., keyboard takes input from user
Computer needs to communicate with I/O device
  E.g., computer takes input from keyboard
Communication through shared memory locations
  Processor and I/O can read/write those memory locations
  Sometimes, data in memory locations can be set/cleared automatically (by hardware) depending on a read/write
Notes: I/O对于计算机系统的意义；2. I/O设备的操作；3. 计算机与外设之间通过共享内存地址进行通信

## Slide 8: I/O: Connecting to the Outside World
Examples
  Keyboard/mouse input, video output on a standard computer
  Network input/output that enables web surfing
  Information from an engine of a car that a computer uses to determine how to tune the engine (output from computer tunes the engine)
  Requests for airline reservations and replies that service those requests
Types of I/O devices characterized by:
  behavior: input, output, storage
    input: keyboard, motion detector, network interface
    output: display screen(monitor), printer, network interface
    storage: disk, CD-ROM
  data rate: how fast can data be transferred?
    keyboard: 100 bytes/sec
    disk: 60-120 MB/s
    network: 1 Mb/s - 100 Gb/s
Notes: I/O设备举例；2. I/O设备分类：（1）输入输出行为；（2）数据传输速率
airline reservations：机票预订

## Slide 9: I/O Controller
Control/Status Registers
  CPU tells device what to do -- write to control register
  CPU checks whether task is done -- read status register
Data Registers
  CPU transfers data to/from device
Device electronics
  performs actual operation
    pixels to screen, bits to/from disk, characters from keyboard
Graphics Controller
Control/Status
Output Data
Electronics
CPU
display
Notes: 简单的I/O控制器主要包括三个部分：（1）控制/状态寄存器；（2）数据寄存器；（3）电子外设

## Slide 10: Programming Interface
How are device registers identified?
  Memory-mapped vs. special instructions
How is timing of transfer managed?
  Asynchronous vs. synchronous
Who controls transfer?
  CPU (polling) vs. device (interrupts)
Notes: 1. 如何定位设备寄存器；2. 数据传输的方式；3. 由谁来控制传输
polling and interrupt轮询与中断

## Slide 11: Memory-Mapped vs. I/O Instructions
Instructions
  PDP-8 (from DEC, 1965)
  designate opcode(s) for I/O
  register and operation encoded in instruction
Memory-mapped
  assign a memory address to each device register
  use data movement instructions (LD/ST) for control and data transfer
0xFE00

## Slide 12: Transfer Timing
I/O events generally happen much slower than CPU cycles.
  If : CPU 300MHz, 10clocks/character,6characters/word
  Then: typing speed (300x106)/(10x6)=5x106words/s
Synchronous
  data supplied at a fixed, predictable rate
  CPU reads/writes every X cycles
Asynchronous
  data rate less predictable
  CPU must synchronize with device, so that it doesn’t miss data or write too quickly
Notes: 1. I/O事件通常比CPU的时钟周期慢很多，假设一个处理器需要消耗10个clocks来完成1个字符的读写过程，平均每个word有6个字符；2. 同步的方式，要求数据以固定的频率产生，CPU以固定的频率读取或者写入，对于打字来说显然是做不到的；3. 如果数据供应的速率不确定，就需要用异步的方式，虽然是异步，但是仍然需要CPU和设备间进行同步，否则会丢失数据或者写太快

## Slide 13: Transfer Control
Who determines when the next data transfer occurs?
  CPU vs. I/O device
Polling is explicitly looking/examining
  CPU keeps checking status register until new data arrives OR device ready for next data
  “Are you there yet? Are you there yet? Are you there yet?”
Interrupts is a nudge, knock on the door, loud noise, which forces you to pay attention
  Device sends a special signal to CPU when new data arrives OR device ready for next data
  CPU can be performing other tasks instead of polling device.
  “Wake me when you get there.”
Notes: Polling：轮询
Nudge窗口抖动

## Slide 14: LC-3
Memory-mapped I/O (Table A.1)
Asynchronous devices
  synchronized through status registers
Polling and Interrupts
Location | I/O Register | Function
xFE00 | Keyboard Status Reg (KBSR) | Bit [15] is one when keyboard has received a new character.
xFE02 | Keyboard Data Reg (KBDR) | Bits [7:0] contain the last character typed on keyboard.
xFE04 | Display Status Register (DSR) | Bit [15] is one when device ready to display another char on screen.
xFE06 | Display Data Register (DDR) | Character written to bits [7:0] will be displayed on screen.
Notes: LC-3采用的I/O方式：内存映射I/O，异步的设备访问方式，轮询或者中断的交互方法

## Slide 15: Memory Map of the LC-3
PC
R4(Global pointer)
R6 (stack pointer)
Device Register
Addresses
0x0000
0xFFFF
Trap Vector Table
Interrupt Vector Table
Operating System
and Supervisor Stack
0x00FF
0x0100
0x01FF
0x0200
0x2FFF
0x3000
0xFDFF
0xFE00
Run-time stack
Program Text
Global data section
Heap (for dynamically
allocated memory)
R5 (frame pointer)
R5
Function2
R6
R5
R6
Function3
Function1
R5
R6

## Slide 16: Organization of Memory of the LC-3
Device Register
Addresses
0x0000
0xFFFF
Trap Vector Table
Interrupt Vector Table
Operating System
and Supervisor Stack
0x00FF
0x0100
0x01FF
0x0200
0x2FFF
0x3000
0xFDFF
0xFE00
Run-time stack
Program Text
Global data section
Heap (for dynamically
allocated memory)
Privileged Memory
System Space
User Space
User Stack
I/O Page
PC
SSP
USP
Supervisor Stack

## Slide 17: Example: Processor Input from Keyboard
When a character is typed:
  its ASCII code is placed in bits [7:0] of KBDR (bits [15:8] are always zero)
  the “ready bit” (KBSR[15]) is set to one
  keyboard is disabled -- any typed characters will be ignored
When KBDR is read:
  KBSR[15] is set to zero, meaning no keyboard key is pending
  keyboard is enabled
KBSR
KBDR
15
8
7
0
15
14
0
keyboard data
ready bit

## Slide 18: Memory-mapped Operations
How do we read ready bit?
How do we test whether the bit is one?
How do we read keyboard data?
Notes: CPU如何读取键盘输入呢？（1）首先需要检查键盘输入是否ready？需要读取ready bit。用LDI读取KBSR寄存器在内存中的映射地址；（2）然后需要判断ready bit是否为1，用BRzp判断ready bit是否为1；（3）最后需要读取键盘输入的数据，用LDI读取KBDR寄存器在内存中的映射地址。

## Slide 19: Basic Input Routine
new
char?
read character
YES
NO
Polling
POLL LDI R0, KBSR BRzp POLL LDI R0, KBDR
...
KBSR .FILL xFE00 KBDR .FILL xFE02
Notes: 轮询方式：

## Slide 20: Memory-mapped I/O
MEM.EN，READ/WRITE
16
ADDR.CTL
LOGIC
MEMORY
MDR
LD.MDR
MUX
MIO.EN
GateMDR
16
MAR
16
LD.MAR
KBDR
KBSR
DDR
DSR
INMUX
16
16
16
16
16
16
16
MEM.R,W
INPUT
OUTPUT
MIO.EN
2
16
2
LD.DDR
16

## Slide 21
SR1
16
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
MEM.EN,R,W
16
GatePC
OUTPUT
MEMORY
MUX
MUX
MDR
…
+
16
16
16
16
ADDR1MUX
2
PCMUX
+1
16
MARMUX
SEXT
[7:0]
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
LD.MDR
MUX
MIO.EN
GateMDR
16
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
GateALU
LOGIC
16
LD.CC
PC
MAR
16
LD.MAR
LDI (Indirect)
EA
OP
EX
S
F
D

## Slide 22
16
16
GatePC
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
LD.MAR
OUTPUT
MUX
MUX
…
+
16
16
16
16
ADDR1MUX
MARMUX
SEXT
[7:0]
GateMARMUX
16
16
16
ADDR2MUX
GateMDR
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
16
PC
2
PCMUX
+1
LD.PC
MEM.EN,R,W
16
MAR
MEMORY
MDR
LD.MDR
MUX
16
MIO.EN
LDI (Indirect)
EA
OP
EX
S
F
D

## Slide 23
RUN
LD.CC
MEM.EN,R,W
16
MAR
16
LD.MAR
PC
GatePC
ALU
A
B
SR2MUX
INPUT
OUTPUT
MEMORY
FINITE STATE MACHINE
MUX
MUX
N
Z
P
LOGIC
16
16
…
+
16
16
16
16
DR
LD.REG
SR2
SR1
ALUK
REG FILE
SR1
OUT
SR2
OUT
16
16
GateALU
16
16
ADDR1MUX
2
3
3
3
PCMUX
+1
16
MARMUX
SEXT
SEXT
SEXT
SEXT
SEXT
[10:0]
[8:0]
[5:0]
[4:0]
[7:0]
16
16
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
MUX
MIO.EN
16
16
16
16
2
LD.IR
IR
16
MDR
LD.MDR
GateMDR
LDI (Indirect)
EA
OP
EX
S
F
D

## Slide 24
16
16
MEMORY
16
N
Z
P
LOGIC
LD.CC
PCMUX
+1
16
16
GatePC
2
LD.PC
16
16
[10:0]
16
16
16
SEXT
SEXT
SEXT
[5:0]
[4:0]
SEXT
[7:0]
16
INPUT
MEM.EN,R,W
16
OUTPUT
MDR
16
LD.MDR
MUX
MIO.EN
GateMDR
16
16
ALU
2
16
GateALU
LDI (Indirect)
SR2
3
16
A
B
ALUK
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
SR1
SR2MUX
16
LD.IR
SEXT
PC
MUX
MUX
…
+
16
ADDR1MUX
MARMUX
GateMARMUX
16
ADDR2MUX
16
FINITE STATE MACHINE
IR
16
EA
D
F
OP
EX
S
MAR
16
RUN
[8:0]
LD.MAR
Notes: PC+Sext(PCOffset9) -> MAR;

## Slide 25
16
SR2
3
+
16
MARMUX
SEXT
[7:0]
GateMARMUX
16
16
16
DR
LD.REG
3
16
PC
2
PCMUX
+1
LD.PC
16
GatePC
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
LD.MAR
OUTPUT
MUX
MUX
…
16
16
16
ADDR1MUX
ADDR2MUX
GateMDR
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
REG FILE
SR1
OUT
SR2
OUT
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
MEM.EN,R,W
16
MAR
MEMORY
MDR
LD.MDR
MUX
16
MIO.EN
LDI (Indirect)
OP
EX
S
D
F
EA
Notes: M[PC+PCOffset9] -> MDR

## Slide 26
16
MEM.EN,R,W
16
MUX
MIO.EN
16
SR2
3
+
16
MARMUX
SEXT
[7:0]
GateMARMUX
16
16
16
DR
LD.REG
3
16
PC
2
PCMUX
+1
LD.PC
GatePC
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
OUTPUT
MUX
MUX
…
16
16
16
ADDR1MUX
ADDR2MUX
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
REG FILE
SR1
OUT
SR2
OUT
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
MAR
MEMORY
MDR
LD.MDR
LDI (Indirect)
EA
EX
S
D
F
OP
GateMDR
16
LD.MAR
Notes: M[PC+PCOffset9] -> MDR -> MAR

## Slide 27: Memory-mapped I/O: LDI R0, KBSR
16
KBDR
16
GateMDR
2
16
MEM.EN，READ/WRITE
MEMORY
16
DDR
DSR
16
16
16
16
MEM.R,W
OUTPUT
16
LD.DDR
16
MAR
LD.MAR
ADDR.CTL
LOGIC
MDR
MUX
MIO.EN
INMUX
16
2
LD.MDR
KBSR
16
INPUT
MIO.EN
Notes: 如果是LDI R0, KBSR：MAR位于I/O mapping内存区，指向KBSR寄存器，KBSR->MDR

## Slide 28: Memory-mapped I/O: LDI R0, KBDR
KBSR
16
16
GateMDR
2
16
MEM.EN，READ/WRITE
MEMORY
16
DDR
DSR
16
16
16
16
MEM.R,W
OUTPUT
16
LD.DDR
16
MAR
LD.MAR
ADDR.CTL
LOGIC
MDR
MUX
MIO.EN
INMUX
16
2
LD.MDR
INPUT
MIO.EN
KBDR
16
Notes: 如果是LDI R0, KBSR，KBDR->MDR

## Slide 29
LD.IR
MEM.EN,R,W
16
MAR
16
LD.MAR
MEMORY
3
SR1
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
PC
GatePC
OUTPUT
MUX
MUX
+
16
16
16
16
ADDR1MUX
2
PCMUX
+1
16
MARMUX
SEXT
[7:0]
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
LD.MDR
MUX
MIO.EN
16
16
16
ALU
A
B
ALUK
2
16
16
GateALU
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
16
…
FINITE STATE MACHINE
N
Z
P
RUN
LOGIC
16
LD.CC
IR
MDR
GateMDR
LDI (Indirect)
EA
OP
S
D
F
EX

## Slide 30: Example: Processor Output to Screen
When Display device is ready to display another character:
  the “ready bit” (DSR[15]) is set to one, indicating that processor can write a character for display
When data is written to the Display data register:
  DSR[15] automatically set to 0
  character in DDR[7:0] is displayed
  any other character data written to DDR is ignored (while DSR[15] is zero)
DSR
DDR
15
8
7
0
15
14
0
output data
ready bit

## Slide 31: Basic Output Routine
screen
ready?
write character
YES
NO
Polling
POLL LDI R1, DSR BRzp POLL STI R0, DDR
...
DSR .FILL xFE04 DDR .FILL xFE06

## Slide 32
SR1
16
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
MEM.EN,R,W
16
GatePC
OUTPUT
MEMORY
MUX
MUX
MDR
…
+
16
16
16
16
ADDR1MUX
2
PCMUX
+1
16
MARMUX
SEXT
[7:0]
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
LD.MDR
MUX
MIO.EN
GateMDR
16
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
GateALU
LOGIC
16
LD.CC
PC
MAR
16
LD.MAR
STI (Indirect)
EA
OP
EX
S
F
D

## Slide 33
16
16
GatePC
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
LD.MAR
OUTPUT
MUX
MUX
…
+
16
16
16
16
ADDR1MUX
MARMUX
SEXT
[7:0]
GateMARMUX
16
16
16
ADDR2MUX
GateMDR
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
16
PC
2
PCMUX
+1
LD.PC
MEM.EN,R,W
16
MAR
MEMORY
MDR
LD.MDR
MUX
16
MIO.EN
STI (Indirect)
EA
OP
EX
S
F
D

## Slide 34
RUN
LD.CC
MEM.EN,R,W
16
MAR
16
LD.MAR
PC
GatePC
ALU
A
B
SR2MUX
INPUT
OUTPUT
MEMORY
FINITE STATE MACHINE
MUX
MUX
N
Z
P
LOGIC
16
16
…
+
16
16
16
16
DR
LD.REG
SR2
SR1
ALUK
REG FILE
SR1
OUT
SR2
OUT
16
16
GateALU
16
16
ADDR1MUX
2
3
3
3
PCMUX
+1
16
MARMUX
SEXT
SEXT
SEXT
SEXT
SEXT
[10:0]
[8:0]
[5:0]
[4:0]
[7:0]
16
16
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
MUX
MIO.EN
16
16
16
16
2
LD.IR
IR
16
MDR
LD.MDR
GateMDR
STI (Indirect)
EA
OP
EX
S
F
D

## Slide 35
16
16
MEMORY
16
N
Z
P
LOGIC
LD.CC
PCMUX
+1
16
16
GatePC
2
LD.PC
16
16
[10:0]
16
16
16
SEXT
SEXT
SEXT
[5:0]
[4:0]
SEXT
[7:0]
16
INPUT
MEM.EN,R,W
16
OUTPUT
MDR
16
LD.MDR
MUX
MIO.EN
GateMDR
16
16
ALU
2
16
GateALU
STI (Indirect)
SR2
3
16
A
B
ALUK
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
SR1
SR2MUX
16
LD.IR
SEXT
PC
MUX
MUX
…
+
16
ADDR1MUX
MARMUX
GateMARMUX
16
ADDR2MUX
16
FINITE STATE MACHINE
IR
16
EA
D
F
OP
EX
S
MAR
16
RUN
[8:0]
LD.MAR

## Slide 36
PC
2
PCMUX
+1
LD.PC
16
16
16
GatePC
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
LD.MAR
OUTPUT
MUX
MUX
…
+
16
16
16
16
ADDR1MUX
MARMUX
SEXT
[7:0]
GateMARMUX
16
16
16
ADDR2MUX
GateMDR
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
MEM.EN,R,W
16
MAR
MEMORY
MDR
LD.MDR
MUX
16
MIO.EN
STI (Indirect)
EA
OP
EX
S
D
F

## Slide 37
MEMORY
16
MEM.EN,R,W
16
MUX
MIO.EN
16
SR2
3
+
16
MARMUX
SEXT
[7:0]
GateMARMUX
16
16
16
DR
LD.REG
3
16
PC
2
PCMUX
+1
LD.PC
GatePC
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
OUTPUT
MUX
MUX
…
16
16
16
ADDR1MUX
ADDR2MUX
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
REG FILE
SR1
OUT
SR2
OUT
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
MAR
MDR
LD.MDR
STI (Indirect)
EA
EX
S
D
F
OP
GateMDR
16
LD.MAR

## Slide 38
16
16
SEXT
[10:0]
16
16
16
SEXT
[7:0]
[8:0]
16
MUX
ADDR2MUX
GateMDR
N
Z
P
LOGIC
16
LD.CC
16
DR
3
LD.REG
SR2
3
16
PC
GatePC
2
PCMUX
+1
16
LD.PC
16
16
LD.IR
MEM.EN,R,W
16
MAR
16
LD.MAR
MEMORY
SR2MUX
16
16
SEXT
SEXT
[5:0]
[4:0]
SEXT
INPUT
OUTPUT
16
16
ALU
A
B
ALUK
2
16
GateALU
SR1
OUT
…
FINITE STATE MACHINE
RUN
IR
MDR
STI (Indirect)
MUX
+
16
ADDR1MUX
MARMUX
GateMARMUX
16
16
REG FILE
SR2
OUT
3
SR1
16
LD.MDR
MUX
MIO.EN
16
F
EA
OP
D
EX
OP
Notes: SR1 -> MDR

## Slide 39: Memory-mapped I/O: STI R0, DDR ?
16
16
MEM.EN，READ/WRITE
ADDR.CTL
LOGIC
MEMORY
MDR
LD.MDR
MUX
MIO.EN
GateMDR
16
KBDR
KBSR
DSR
INMUX
16
16
16
16
MEM.R,W
INPUT
OUTPUT
MIO.EN
2
16
2
16
MAR
16
LD.MAR
DDR
LD.DDR
16
16

## Slide 40: Keyboard Echo Routine
Usually, input character is also printed to screen.
  User gets feedback on character typed and knows its ok to type the next character.
new
char?
read character
YES
NO
screen
ready?
write character
YES
NO
POLL1 LDI R0, KBSR BRzp POLL1 LDI R0, KBDR POLL2 LDI R1, DSR BRzp POLL2 STI R0, DDR
...
KBSR .FILL xFE00 KBDR .FILL xFE02 DSR .FILL xFE04 DDR .FILL xFE06
Notes: 键盘回显的例子，输入字符的同时，显示在屏幕上