## Slide 1: Chapter 9-3 Interrupt-Driven I/O
陈俊仕
cjuns@ustc.edu.cn 2024 Fall
计算机科学与技术学院
School of Computer Science and Technology
计算系统概论A
Introduction to Computing Systems
（ CS1002A.03 ）

## Slide 2
Outline
Review
1
2
From ENIAC to the Stored Program Computer
Review
1
2
Interrupt-Driven I/O
2
From ENIAC to the Stored Program Computer
3
Input/Output

## Slide 3: What is Interrupt-Driven I/O?
Program A is executing instruction n
Program A is executing instruction n+1
Program A is executing instruction n+2
Program A is executing instruction n+3
Program A is executing instruction n+4
  ……
  ……
  ……

## Slide 4: What is Interrupt-Driven I/O?
Program A is executing instruction n
Program A is executing instruction n+1
Program A is executing instruction n+2
Interrupt!!!
Program A is executing instruction n+3
Program A is executing instruction n+4
  ……
  ……
  ……

## Slide 5: What is Interrupt-Driven I/O?
Program A is executing instruction n
Program A is executing instruction n+1
Program A is executing instruction n+2
1: Interrupt signal is detected
1: Program A is put into suspended animation
1: PC is loaded with the starting address of Program B
2: Program B starts satisfying I/O device’s needs
2: Program B continues satisfying I/O device’s needs
2: Program B continues satisfying I/O device’s needs
2: Program B finishes satisfying I/O device’s needs
3: Program A is brought back to life
Program A is executing instruction n+3
Program A is executing instruction n+4
  ……
  ……
  ……

## Slide 6: When and Why to Use Interrupts
When timing of external event is uncertain
  Example: incoming packet from network
  TRAP vs. Interrupt, 12.5s vs. 0.00001s @ 100 char read from KB
When device operation takes a long time
  Example: start a disk transfer, disk interrupts when transfer is finished
  processor can do something else in the meantime
When event is rare but critical
  Example: building on fire -- save and shut down!

## Slide 7: How to implement an interrupt
To implement an interrupt mechanism, we need:
  A way for the I/O device to signal the CPU that an interesting event has occurred.
  A way for the CPU to test whether the interrupt signal is set.
Generating Signal
  Software sets "interrupt enable(IE)" bit in device register.
  When ready bit is set and IE bit is set, interrupt is signaled.
KBSR
15
14
0
ready bit
13
interrupt enable bit
interrupt signal to processor

## Slide 8: Interrupt-Driven I/O
Testing for Interrupt Signal
  CPU looks at signal between STORE and FETCH phases
  If not set, continues with next instruction
  If set, transfers control to Interrupt Service Routine(ISR)
EA
OP
EX
S
F
D
interrupt
signal?
Transfer to
ISR
NO
YES
More details in Chapter 10.

## Slide 9: Interrupt-Driven I/O
Timing of I/O controlled by device
  1. Report: Tells processor when something interesting happens
    Example: when character is entered on keyboard
    Example: when monitor is ready for next character
    Example: when block has been transferred from disk to memory
  2. Processing: Processor interrupts its normal instruction processing and executes a Interrupt Service Routine(ISR) (like a TRAP)
    1. Figure out what device is causing the interrupt
    2. Execute routine to deal with event
    3. Resume execution
No need for processor to poll device
  Can perform other useful work
Interrupt is an unscripted subroutine call,
triggered by an external event

## Slide 10: How is Interrupt Signaled?
External interrupt signal by Devices: INT
  Device sets INT=1 when it wants to cause an interrupt
Interrupt vector: INTV
  8-bit signal for device to identify itself
  Also used as entry into Interrupt Vector Table, which gives starting address of Interrupt Service Routine (ISR)
    Just like Trap Vector Table and Trap Service Routine
    TVT: x0000 to x00FF
    IVT: x0100 to x01FF

## Slide 11: Memory Model in the LC-3
PC
R4(Global pointer)
R6 (stack pointer)
Device Register
Addresses
0x0000
0xFFFF
Trap Vector Table
Interrupt Vector Table
Operating System
and Supervisor Stack
0x00FF
0x0100
0x01FF
0x0200
0x2FFF
0x3000
0xFDFF
0xFE00
Run-time stack
Program Text
Global data section
Heap (for dynamically
allocated memory)
R5 (frame pointer)
R5
Function2
R6
R5
R6
Function3
Function1
R5
R6
IVT

## Slide 12: Interrupt Signal to CPU
Several things must be true for an I/O device to actually interrupt the processor (ALL the three elements are present)
  The I/O device must want service(ready bit = 1)
  The device must have the right to request the service(interrupt enable bit = 1).
  The device request must be more urgent than what the processor is currently doing.

## Slide 13: Interrupt Signal to CPU
At the device side(I/O device set)
  Control register has “Interrupt Enable” bit
  Must be set for interrupt to be generated
At the processor(CPU set)
  Sometimes have “Interrupt Mask” register (LC-3 does not)
  When set, processor ignores INT signal
  Why? - Example: may not want to be interrupted while in ISR
KBSR
15
14
0
I/O device set: ready bit
13
CPU set: interrupt enable bit
interrupt signal to processor(INT)

## Slide 14: The Processor State Register(PSR)
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
Pr
PL
N
Z
P
PSR
Cond Codes
Priority Level
The Processor Status Register
PSR[15]
  0, privileged (supervisor) mode
  1, unprivileged(user)mode
The Priority Level of a program being executed
  PL[10:8]
  0(最低)~7(最高)
Priv Mode

## Slide 15: Generation of the Interrupt Signal to CPU
PL1
Device
14
0
13
PL2
Device
14
0
13
PL7
Device
14
0
13
Priority encoder
INT
B
A
?
A>B
PL of executing program
…...
What if more than one device wants to interrupt?
  External logic controls which one gets to drive signals
Notes: PL；Priority Level

## Slide 16: Testing for Interrupt Signal
CPU looks at signal between STORE and FETCH phases
If not set, continues with next instruction
If set, transfers control to interrupt service routine
EA
OP
EX
S
F
D
interrupt
signal?
Transfer to
ISR
NO
YES

## Slide 17: How Does Processor Handle It?
Examines INT signal just before starting FETCH phase
  If INT=1, don’t fetch next instruction
  Instead
    Save program state (PC, PSR (privilege and CCs)) on stack
    Update PSR (set privilege bit)
    Index INTV into IVT to get start address of ISR (put in PC)
After service routine
  RTI instruction restores PSR and PC from stack
  Need a different return instruction, because
    RET gets PC from R7 and doesn’t update PSR
Processor only checks between STORE and FETCH phases -- Why?

## Slide 18: Supervisor Mode and the Stack
Problem
  PC and PSR shouldn’t be saved on user stack
  What if R6 is uninitialized?
  What if user has set R6 to refer to OS memory?
  User could see OS data (when trap returns)
Solution
  Create two versions of R6 (stack pointer) in register file
    One is user stack pointer (what we’ve been using all along)
    The other is supervisor stack pointer
  Extra register file logic selects the appropriate register based on privilege bit in current PSR
  Bottom line: OS code always uses its own stack

## Slide 19: An Example (0)

## Slide 20: An Example (1)
x8001

## Slide 21: An Example (2)
x0001
x8001

## Slide 22: An Example (3)
x0002
x8001

## Slide 23: An Example (4)
x0002
x0002
x8001

## Slide 24: An Example (5)
x0002
x0002
x8001

## Slide 25: An Example (6)
x8001
x8001