## Slide 1: Chapter 3-1 Transistors & Logic Gates
计算机系统概论
Introduction to Computing Systems
（CS1002A.02）
苗付友
mfy@ustc.edu.cn 2023 Fall
计算机科学与技术学院
School of Computer Science and Technology

## Slide 2
Outline
Review
1
3
Logic Gates
2
The Transistor
4
Summary

## Slide 3
Outline
Review
1
3
Logic Gates
2
The Transistor
4
Summary

## Slide 4: Review
Great Idea #0: Great Idea from Ancient Chinese Philosophy(Bits and Bytes)
How do we represent data in a computer?
  Bits: 0/1
  Data type: representation and operations within the computer
    Integer Data Types
      Unsigned Integers
      2’Complement Integers
    Fixed-Point Data Types
    Floating-Point Data Types
    Text – characters, strings, …
    Images – pixels, colors, shapes, …
    Sound
    Instructions
    ……
  Arithmetic and Logical Operations
  Binary-Decimal Conversion

## Slide 5: Today
Microprocessors contain millions of transistors
  Intel Core 2 Duo: 291 million
  AMD Barcelona: 463 million
  IBM Power6: 790 million
Transistor: Building Block of Computers
  Logically, each transistor acts as a switch
Combined to implement logic functions
  AND, OR, NOT

## Slide 6: Approach: Bottom Up
Transistor Physical Layout
Scheme for
Representing Information
Register Transfer Level (RTL) Design
1K~10K Cells/Module
(100K Devices)
ALU
Full Adder
Gate Level Design
Circuit Level Design
（Transistor Level Design）
(2~8 Devices/Gate)
Register Transfer Level (RTL) Design
2~16 Gates/Cell
(16~64 Devices)
Clk
Register
+
Cout
S
A
B
Cin
Integrated Circuit Design
100 Modules/ IC
0.25M~20G Devices
Now, You are Here.

## Slide 7: Great Idea #3: Abstraction Helps Us Manage Complexity
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 8: Great Idea #4: Software and Hardware Co-design
Software
Hardware
Application
Language
Machine Architecture, ISA
Microarchiture
Logic and IC
Device
Algorithm & Data Structure
Computer System: Layers of Abstraction
Now, You are Here.
Notes: 8

## Slide 9
Outline
Review
1
3
Logic Gates
2
The Transistor
4
Summary

## Slide 10: Vacuum tubes used as switches
Switch open:
  No current through circuit
  Light is off
  Vout is +2.9V
Switch closed:
  Short circuit across switch
  Current flows
  Light is on
  Vout is 0V
Switch-based circuits can easily represent two states:
on/off, open/closed, voltage/no voltage.
Notes: 10

## Slide 11: Vacuum tubes used as switches made electronic computing
1946，the ENIAC computer used 17,468 vacuum tubes and consumed 150 kW of power
Vacuum tubes used as switches made electronic computing possible for the first time, but the cost and relatively short mean time to failure of tubes were limiting factors."The common wisdom was that valves—which, like light bulbs, contained a hot glowing filament—could never be used satisfactorily in large numbers, for they were unreliable, and in a large installation too many would fail in too short a time".Tommy Flowers, who later designed Colossus, "discovered that, so long as valves were switched on and left on, they could operate reliably for very long periods, especially if their 'heaters' were run on a reduced current". In 1934 Flowers built a successful experimental installation using over 3,000 tubes in small independent modules; when a tube failed, it was possible to switch off one module and keep the others going, thereby reducing the risk of another tube failure being caused; this installation was accepted by the Post Office (who operated telephone exchanges). Flowers was also a pioneer of using tubes as very fast (compared to electromechanical devices) electronic switches. Later work confirmed that tube unreliability was not as serious an issue as generally believed; the 1946 ENIAC, with over 17,000 tubes, had a tube failure (which took 15 minutes to locate) on average every two days. The quality of the tubes was a factor, and the diversion of skilled people during the Second World War lowered the general quality of tubes. During the war Colossus was instrumental in breaking German codes. After the war, development continued with tube-based computers including, military computers ENIAC and Whirlwind, the Ferranti Mark 1 (one of the first commercially available electronic computers), and UNIVAC I, also available commercially.
Advances using subminiature tubes included the Jaincomp series of machines produced by the Jacobs Instrument Company of Bethesda, Maryland. Models such as its Jaincomp-B employed just 300 such tubes in a desktop-sized unit that offered performance to rival many of the then room-sized machines.

## Slide 12: The invention of the transistor
Bell Labs lays the groundwork
1945: Bell sets up lab in the hopes of developing “solid state” components to replace existing electromechanical systems. William Schockley, John Bardeen, Walter Brattain: all solid-state physicists. Focus on Si and Ge.
1947：The Invention of the First Transistor- the point-contact transistor
1951: Shockley develops junction transistor which can be manufactured in quantity.
1954: The first transistor radio! Also, TI makes first silicon transistor (price $2.50)
1956: Bardeen, Shockley, Brattain receive Nobel Prize.

## Slide 13: Transistor as a switch
Switch open:
  No current through circuit
  Light is off
  Vout is +2.9V
Switch closed:
  Short circuit across switch
  Current flows
  Light is on
  Vout is 0V
Switch-based circuits can easily represent two states:
on/off, open/closed, voltage/no voltage.
Notes: 13

## Slide 14: N-type MOS Transistor
MOS = Metal Oxide Semiconductor
  two types: N-type and P-type
N-type metal–oxide–semiconductor (NMOS)
N-type
  when Gate has positive voltage, short circuit between #1 and #2 (switch closed)
  when Gate has zero voltage, open circuit between #1 and #2 (switch open)
Gate = 1
Gate = 0
Terminal #2 must be
connected to GND (0V).
Notes: 14

## Slide 15: P-type MOS Transistor
P-type metal–oxide–semiconductor (PMOS)
P-type is complementary to N-type
  when Gate has positive voltage, open circuit between #1 and #2 (switch open)
  when Gate has zero voltage, short circuit between #1 and #2 (switch closed)
Gate = 1
Gate = 0
Terminal #1 must be
connected to +2.9V.
Notes: 15

## Slide 16: Logic Gates
Use switch behavior of MOS transistors to implement logical functions: AND, OR, NOT.
Digital symbols:
  recall that we assign a range of analog voltages to each digital (logic) symbol
  assignment of voltage ranges depends on electrical properties of transistors being used
    typical values for "1": +5V, +3.3V, +2.9V, +1.1V
    for purposes of illustration, we'll use +2.9V

## Slide 17: CMOS Circuit
CMOS: Complementary MOS
Uses both N-type and P-type MOS transistors
  P-type
    Attached to + voltage
    Pulls output voltage UP when input is zero
  N-type
    Attached to GND
    Pulls output voltage DOWN when input is one
For all inputs, make sure that output is either connected to GND or to +,but not both!

## Slide 18: A transistor under a microscope
http://www.zhihu.com/question/26998618
  How is it possible to have tens of millions of transistors in a chip?
显微镜下的intel 14纳米晶体管

## Slide 19: Microprocessors contain millions of transistors

## Slide 20: Microprocessors contain millions of transistors

## Slide 22
Outline
Review
1
3
Logic Gates
2
The Transistor
4
Summary

## Slide 23: Approach: Bottom Up
Transistor Physical Layout
Scheme for
Representing Information
Register Transfer Level (RTL) Design
1K~10K Cells/Module
(100K Devices)
ALU
Full Adder
Gate Level Design
Circuit Level Design
（Transistor Level Design）
(2~8 Devices/Gate)
Register Transfer Level (RTL) Design
2~16 Gates/Cell
(16~64 Devices)
Clk
Register
+
Cout
S
A
B
Cin
Integrated Circuit Design
100 Modules/ IC
0.25M~20G Devices
Now, You are Here.

## Slide 24: Great Idea #3: Abstraction Helps Us Manage Complexity
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 25: Great Idea #4: Software and Hardware Co-design
Software
Hardware
Application
Language
Machine Architecture, ISA
Microarchiture
Logic and IC
Device
Algorithm & Data Structure
Computer System: Layers of Abstraction
Now, You are Here.
Notes: 25

## Slide 26: Inverter (NOT Gate)
In | Out
0 V | 2.9 V
2.9 V | 0 V
In | Out
0 | 1
1 | 0
Truth table
2.9V
0V
Notes: 26

## Slide 27: The process of fabrication of a CMOS inverter
Simplified process of fabrication of a CMOS inverter on p-type substrate in semiconductor microfabrication.

## Slide 28: NOR Gate
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Note: Serial structure on top, parallel on bottom.
INPUT |  | OUTPUT
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Notes: 28

## Slide 29: OR Gate
Add inverter to NOR.
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
INPUT |  | OUTPUT
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 30: NAND Gate (AND-NOT)
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Note: Parallel structure on top, serial on bottom.
INPUT |  | OUTPUT
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: 30

## Slide 31: Example: NAND gate in physical layout
The physical layout of a NAND circuit. The larger regions of N-type diffusion and P-type diffusion are part of the transistors. The two smaller regions on the left are taps to prevent latchup.
NAND gate in CMOS logic

## Slide 32: AND Gate
Add inverter to NAND.
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
INPUT |  | OUTPUT
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 33: Basic Gates
From Now on……Gates
  Covered transistors mostly so that you know they exist
  Note: “Logic Gate” not related to “Gate” of transistors
Will study implementation in terms of gates
  Circuits that implement Boolean functions
More complicated gates from transistors possible
  XOR, Multiple-input AND-OR-Invert (AOI) gates

## Slide 34: Practice
Implement a 3-input NOR gate with CMOS.

## Slide 35: Practice
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: 35
In ECE 352, you'll learn how to minimize logic functions -- to implement them with the fewest number of gates.

## Slide 36: More than 2 Inputs?
AND/OR can take any number of inputs.
  AND = 1 if all inputs are 1.
  OR = 1 if any input is 1.
  Similar for NAND/NOR.
Can implement with multiple two-input gates, or with single CMOS circuit.

## Slide 37: Visual Shorthand for Multi-bit Gates
Use a cross-hatch mark to group wires
  Example: calculate the AND of a pair of 4-bit numbers
  A3 is “high-order” or “most-significant” bit
  If “A” is 1000, then A3 = 1, A2 = 0, A1 = 0, A0 = 0

## Slide 38: Shorthand for Inverting Signals
Invert a signal by adding either
  A before/after a gate
  A “bar” over letter

## Slide 39: Logical Completeness
AND, OR, NOT can implement ANY truth table
A | B | C | D
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
1. AND combinations that yield a "1" in the truth table.
2. OR the results of the AND gates.
Notes: 39
Note the use of the bubbles (NOT) in the input.

## Slide 40: Logical Completeness
AND, OR, NOT can implement ANY truth table

## Slide 41: DeMorgan's Law
Converting AND to OR (with some help from NOT)
Consider the following gate:
A | B |  |  |  | 
0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1
Same as A OR B!
To convert AND to OR
(or vice versa),
invert inputs and output.
Why might this be useful?
Notes: 41
If there's time, perhaps discuss how all gates can be implemented with NAND (or NOR).
Therefore, you can implement any truth table using only NAND (or NOR) gates.

## Slide 42
Outline
Review
1
3
Logic Gates
2
The Transistor
4
Summary

## Slide 43: N-type MOS Transistor
MOS = Metal Oxide Semiconductor
  two types: N-type and P-type
N-type
  when Gate has positive voltage, short circuit between #1 and #2 (switch closed)
  when Gate has zero voltage, open circuit between #1 and #2 (switch open)
Gate = 1
Gate = 0
Terminal #2 must be
connected to GND (0V).
Notes: 43

## Slide 44: P-type MOS Transistor
P-type is complementary to N-type
  when Gate has positive voltage, open circuit between #1 and #2 (switch open)
  when Gate has zero voltage, short circuit between #1 and #2 (switch closed)
Gate = 1
Gate = 0
Terminal #1 must be
connected to +2.9V.
Notes: 44

## Slide 45: Gates