## Slide 1: Chapter 3-3 Sequential Logic Circuits
苗付友
mfy@ustc.edu.cn 2023 Fall
计算机科学与技术学院
School of Computer Science and Technology
计算机系统概论
Introduction to Computing Systems
（CS1002A.02）

## Slide 2
Outline
Review
1
3
From Logic to Data Path
2
Sequential Logic Circuits
4
Summary

## Slide 3
Outline
Review
1
3
From Logic to Data Path
2
Sequential Logic Circuits
4
Summary

## Slide 4: Review
We’ve touched on basic digital logic
  Transistors
  Gates
  Storage (latches, flip-flops, register, memory)
Built some simple logical circuits
  adder, subtracter, adder/subtracter，Incrementer
  Counter (consisting of register and incrementer)

## Slide 5: Basic Logical Structure

## Slide 6: Today
A computer as a (simple?) state machine
  State machines
  Programmable traffic sign state machine

## Slide 7: Approach: Bottom Up
Transistor Physical Layout
Scheme for
Representing Information
Register Transfer Level (RTL) Design
1K~10K Cells/Module
(100K Devices)
ALU
Full Adder
Gete Level Design
Circuit Level Design
（Transistor Level Design）
(2~8 Devices/Gate)
Register Transfer Level (RTL) Design
2~16 Gates/Cell
(16~64 Devices)
Clk
Register
+
Cout
S
A
B
Cin
Integrated Circuit Design
100 Modules/ IC
0.25M~20G Devices
Now, You are Here.
And Here.

## Slide 8: Great Idea #3: Abstraction Helps Us Manage Complexity
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 9: Great Idea #4: Software and Hardware Co-design
Software
Hardware
Application
Language
Machine Architecture, ISA
Microarchiture
Logic and IC
Device
Algorithm & Data Structure
Computer System: Layers of Abstraction
Now, You are Here.
Notes: 9

## Slide 10
Outline
Review
1
3
From Logic to Data Path
2
Sequential Logic Circuits
4
Summary

## Slide 11: State Machine
Another type of sequential circuit
  Combines combinational logic with storage
  “Remembers” state, and changes output (and state) based on inputs and current state
State Machine
Combinational
Logic Circuit
Storage
Elements
Inputs
Outputs

## Slide 12: Combinational vs. Sequential
Two types of “combination” locks
4
1
8
4
30
15
5
10
20
25
Combinational
Success depends only on the values, not the order in which they are set.
Sequential
Success depends on the sequence of values
(e.g, R-13, L-22, R-3).

## Slide 13: State
The state of a system is a snapshot of all the relevant elements of the system at the moment the snapshot is taken.
Examples:
  The state of a basketball game can be represented by the scoreboard.
    Number of points, time remaining, possession, etc.

## Slide 14: State of Sequential Lock
Our lock example has four different states, labelled A-D: A: The lock is not open, and no relevant operations have been performed.
B: The lock is not open, and the user has completed the R-13 operation.
C: The lock is not open, and the user has completed R-13, followed by L-22.
D: The lock is open.

## Slide 15: State Diagram
Shows states and actions that cause a transition between states.

## Slide 16: Finite State Machine
A description of a system with the following components:
A finite number of states
A finite number of external inputs
A finite number of external outputs
An explicit specification of all state transitions
An explicit specification of what causes each external output value.
Often described by a state diagram.
  Inputs may cause state transitions.
  Outputs are associated with each state (or with each transition).

## Slide 17: Implementing a Finite State Machine
Combinational logic
  Determine outputs and next state.
Storage elements
  Maintain state representation.
State Machine
Combinational
Logic Circuit
Storage
Elements
Inputs
Outputs
Clock

## Slide 18: The Clock
Frequently, a clock circuit triggers transition from one state to the next.
At the beginning of each clock cycle, state machine makes a transition, based on the current state and the external inputs.
  Not always required. In lock example, the input itself triggers a transition.
“1”
“0”
time
One
Cycle

## Slide 19: Storage: Master-Slave Flipflop
A pair of gated D-latches, to isolate next state from current state.
During 1st phase (clock=1), previously-computed state becomes current state and is sent to the logic circuit.
During 2nd phase (clock=0), next state, computed by logic circuit, is stored in Latch A.

## Slide 20
Storage: Master-Slave Flipflop

## Slide 21: Storage
Each master-slave flip-flop stores one state bit.
The number of storage elements (flip-flops) needed is determined by the number of states (and the representation of each state).
Examples:
  Sequential lock
    Four states – two bits
  Basketball scoreboard
    7 bits for each score, 5 bits for minutes, 6 bits for seconds, 1 bit for possession arrow, 1 bit for half, …

## Slide 22: Complete Example
A blinking traffic sign
  No lights on
  1 & 2 on
  1, 2, 3, & 4 on
  1, 2, 3, 4, & 5 on
  (repeat as long as switch is turned on)
DANGER MOVE RIGHT
1
2
3
4
5

## Slide 23: Traffic Sign State Diagram
State bit S1
State bit S0
Switch on
Switch off
Outputs
Transition on each clock cycle.

## Slide 24: Traffic Sign State Diagram: State 00
Transition on each clock cycle.

## Slide 25: Traffic Sign State Diagram: State 01
Transition on each clock cycle.

## Slide 26: Traffic Sign State Diagram: State 10
Transition on each clock cycle.

## Slide 27: Traffic Sign State Diagram: State 11
Transition on each clock cycle.

## Slide 28: Traffic Sign State Diagram: State 00
Transition on each clock cycle.

## Slide 29: Traffic Sign Truth Tables
Outputs
(depend only on state: S1S0)
S1 | S0 | Z | Y | X
0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1
Lights 1 and 2
Lights 3 and 4
Light 5
Next State: S1’S0’ (depend on state and input)
In | S1 | S0 | S1’ | S0’
0 | X | X | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
Switch
Whenever In=0, next state is 00.

## Slide 30: Traffic Sign Logic
Master-slave flipflop
S’0
S’1
S0
S1
S1 | S0 | Z | Y | X
0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 31
In | S1 | S0 | S1’ | S0’
0 | X | X | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
初始状态
S’1
S’0
S1
S0

## Slide 32
Outline
Review
1
3
From Logic to Data Path
2
Sequential Logic Circuits
4
Summary

## Slide 33: From Logic to Data Path
The data path of a computer is all the logic used to process information.
  See the data path of the LC-3 on next slide.
Combinational Logic
  Decoders -- convert instructions into control signals
  Multiplexers -- select inputs and outputs
  ALU (Arithmetic and Logic Unit) -- operations on data
Sequential Logic
  State machine -- coordinate control signals and data movement
  Registers and latches -- storage elements

## Slide 34
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
MEM.EN,R,W
16
MAR
16
LD.MAR
PC
GatePC
OUTPUT
MEMORY
MUX
MUX
MDR
…
+
16
16
16
16
ADDR1MUX
2
PCMUX
+1
16
MARMUX
SEXT
[7:0]
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
LD.MDR
MUX
MIO.EN
GateMDR
16
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
LC-3 Data Path Overview (Microarchitecture)
Control Unit
Memory Unit
Processing Unit

## Slide 35
Outline
Review
1
3
From Logic to Data Path
2
Sequential Logic Circuits
4
Summary

## Slide 36: Summary
MOS transistors are used as switches to implement logic functions.
  N-type: connect to GND, turn on (with 1) to pull down to 0
  P-type: connect to +2.9V, turn on (with 0) to pull up to 1
Basic gates: NOT, NOR, NAND
  Logic functions are usually expressed with AND, OR, and NOT
Properties of logic gates
  Completeness
    can implement any truth table with AND, OR, NOT
  DeMorgan's Law
    convert AND to OR by inverting inputs and output

## Slide 37: Summary
We’ve touched on basic digital logic
  Transistors
  Gates
  Storage (latches, flip-flops, memory)
  State machines
Built some simple circuits
  adder, subtracter, adder/subtracter，Incrementer
  Counter (consisting of register and incrementer)
  Programmable traffic sign state machine
Up next: a computer as a (simple?) state machine

## Slide 38: LC-3 Data Path

## Slide 39: Next Time
Topic
  The von Neumann Model
Readings
  Chapter 4.0 - 4.2