## Slide 1: Chapter 7 Assembly Language Program
计算机科学与技术学院
School of Computer Science and Technology
计算机系统概论
Introduction to Computing Systems
（ CS1002A.01）

## Slide 2
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary
Review
1
3
Assembly Process
2
Assembly Language Overview
4
Summary

## Slide 3
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary
Review
1
3
Assembly Process
2
Assembly Language Overview
4
Summary

## Slide 4: Review: The Transistor & Basic Logical Structure

## Slide 5: Review: Von Neumann Model

## Slide 6: Review: Von Neumann Model
So far, we’ve learned how to:
  compute with values in registers
  load data from memory to registers
  store data from registers to memory

## Slide 7: Review: The ISA
2023/11/16
7

## Slide 8: Review: The State Machine(Turing Machine equivalent)
2023/11/16
8
EA
OP
EX
S
F
D

## Slide 9: Review: The Data Path(von Neumann Model)
2023/11/16
9

## Slide 10
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary
Review
1
3
Assembly Process
2
Assembly Language Overview
4
Summary

## Slide 11: An LC-3 Program
0 1 0 1 0 1 0 0 1 0 1 0 0 0 0 0
0 0 1 0 0 1 1 0 0 0 0 1 0 0 0 0
1 1 1 1 0 0 0 0 0 0 1 0 0 0 1 1
0 1 1 0 0 0 1 0 1 1 0 0 0 0 0 0
0 0 0 1 1 0 0 0 0 1 1 1 1 1 0 0
0 0 0 0 0 1 0 0 0 0 0 0 1 0 0 0
1 0 0 1 0 0 1 0 0 1 1 1 1 1 1 1
0 0 0 1 0 0 1 0 0 1 1 0 0 0 0 1
0 0 0 1 0 0 1 0 0 1 0 0 0 0 0 0
0 0 0 0 1 0 1 0 0 0 0 0 0 0 0 1
0 0 0 1 0 1 0 0 1 0 1 0 0 0 0 1
0 0 0 1 0 1 1 0 1 1 1 0 0 0 0 1
0 1 1 0 0 0 1 0 1 1 0 0 0 0 0 0
0 0 0 0 1 1 1 1 1 1 1 1 0 1 1 0
0 0 1 0 0 0 0 0 0 0 0 0 0 1 0 0
0 0 0 1 0 0 0 0 0 0 0 0 0 0 1 0
1 1 1 1 0 0 0 0 0 0 1 0 0 0 0 1
1 1 1 1 0 0 0 0 0 0 1 0 0 1 0 1
1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1
0 0 0 0 0 0 0 0 0 0 1 1 0 0 0 0
0 0 0 0 0 0 0 0 0 1 0 0 1 1 0 0
0 0 0 0 0 0 0 0 0 1 0 0 1 0 1 0
0 0 0 0 0 0 0 0 0 1 0 1 0 0 0 1
0 0 0 0 0 0 0 0 0 1 0 0 1 1 0 0
0 0 0 0 0 0 0 0 0 1 0 1 0 1 1 0
0 0 0 0 0 0 0 0 0 1 0 0 1 0 0 1
0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 1
0 0 0 0 0 0 0 0 0 1 0 1 0 0 1 1
0 0 0 0 0 0 0 0 0 1 0 1 0 1 1 0
0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 1 0 1 0 1 1 0
0 0 0 0 0 0 0 0 0 1 0 0 1 0 0 1
0 0 0 0 0 0 0 0 0 1 0 1 1 0 0 0
0 0 0 0 0 0 0 0 0 1 0 0 1 1 0 0
0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 1 0 0 1 0 0 0
0 0 0 0 0 0 0 0 0 1 0 0 1 1 1 0
0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 0
0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 1 0 1 1 0 1 0
0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 0
X4101
X4102
X4103
X4104
X4105
X4106
X4107
X4108
X4109
X410A
X410B
X410C
X410D
X410E
X410F
X4110
X4101
X4102
X4103
X4104
X8001
X8002
X8003
X8004
X8005
X8006
X8007
X8008
X8009
X800A
X800B
X800C
X800D
X800E
X800F
X8010
X8011
X8012
X8013
X8014
X8015
X8016
X8017
X8018

## Slide 12: Human-Readable Machine Language
Computers like ones and zeros…
Humans like symbols…
Assembler (汇编器) is a program that turns symbols into machine instructions.
  ISA-specific: close correspondence between symbols and instruction set
    mnemonics (助记符) for opcodes
    labels (标号) for memory locations
  additional operations for allocating storage and initializing data
ADD R6,R2,R6 ; increment index reg.
or
C = a + b;
0001110010000110

## Slide 13: Great Idea #4: Software and Hardware Co-design
Software
Hardware
Application
Language
Machine Architecture, ISA
Microarchiture
Logic and IC
Device
Algorithm & Data Structure
Computer System: Layers of Abstraction
Now, You are Here.
Notes: 13

## Slide 14: Great Idea #3: Abstraction Helps Us Manage Complexity
Solve a system of equations
Gaussian
elimination
Jacobi
iteration
Red-black SOR
Multigrid
FORTRAN
C
C++
Java
Intel x86
Sun SPARC
IBM PowerPC
Pentium 4
Core 2 Duo
AMD Athlon X2
Ripple-carry adder
Carry-lookahead adder
Static CMOS
Dynamic CMOS
Nanomechanical
Algorithm and Data Structure
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Electronic Devices
Programming Language/Compiler
Analog/Digital Circuits
Physics

## Slide 15: An Assembly Language Program
;
; Program to multiply a number by the constant 6
;
.ORIG x3050
LD R1, SIX
LD R2, NUMBER
AND R3, R3, #0 ; Clear R3. It will
; contain the product.
; The inner loop
;
AGAIN ADD R3, R3, R2
ADD R1, R1, #-1 ; R1 keeps track of
BRp AGAIN ; the iteration.
;
HALT
;
NUMBER .BLKW 1
SIX .FILL x0006
;
.END

## Slide 16: LC-3 Assembly Language Syntax
Each line of a program is one of the following:
  an instruction
  an assembler directive (or pseudo-op, 伪操作)
  a comment
  empty
Whitespace (between symbols) and case are ignored.
Comments (beginning with “;”) are also ignored.
An instruction has the following format:
LABEL OPCODE OPERANDS COMMENTS
optional
mandatory

## Slide 17: Opcodes and Operands 操作码 和 操作数
Opcodes
  reserved symbols that correspond to LC-3 instructions
  listed in Appendix A
    ex: ADD, AND, LD, LDR, …
Operands
  registers -- specified by Rn, where n is the register number
  numbers -- indicated by # (decimal) or x (hex)
  label -- symbolic name of memory location
  separated by comma
  number, order, and type correspond to instruction format
    ex: ADD R1,R1,R3 ADD R1,R1,#3 LD R6,NUMBER BRz LOOP

## Slide 18: Labels and Comments 标号 和 注释
Label
  placed at the beginning of the line
  assigns a symbolic name to the address corresponding to line
    ex: LOOP ADD R1,R1,#-1 BRp LOOP
Comment
  anything after a semicolon (; 分号) is a comment
  ignored by assembler
  used by humans to document/understand programs
  tips for useful comments:
    avoid restating the obvious, as “decrement R1”
    provide additional insight, as in “accumulate product in R6”
    use comments to separate pieces of program

## Slide 19: Assembler Directives (指示符)
Pseudo-operations
  do not refer to operations executed by program
  used by assembler
  look like instruction, but “opcode” starts with dot
Opcode | Operand | Meaning
.ORIG | address | starting address of program
.END |  | end of program
.BLKW | n | allocate n words of storage
.FILL | n | allocate one word, initialize with value n
.STRINGZ | n-character string | allocate n+1 locations, initialize w/characters and null terminator

## Slide 20: Example
.ORIG X3010
HELLO .STRINGZ ”Hello, World!”
x3010: x0048 x3011: x0065 x3012: x006C x3013: x006C x3014: x006F x3015: x002C x3016: x0020 x3017: x0057 x3018: x006F x3019: x0072 x301A: x006C x301B: x0064 x301C: x0021 x301D: x0000
00 | nul | 10 | dle | 20 | sp | 30 | 0 | 40 | @ | 50 | P | 60 | ` | 70 | p
01 | soh | 11 | dc1 | 21 | ! | 31 | 1 | 41 | A | 51 | Q | 61 | a | 71 | q
02 | stx | 12 | dc2 | 22 | " | 32 | 2 | 42 | B | 52 | R | 62 | b | 72 | r
03 | etx | 13 | dc3 | 23 | # | 33 | 3 | 43 | C | 53 | S | 63 | c | 73 | s
04 | eot | 14 | dc4 | 24 | $ | 34 | 4 | 44 | D | 54 | T | 64 | d | 74 | t
05 | enq | 15 | nak | 25 | % | 35 | 5 | 45 | E | 55 | U | 65 | e | 75 | u
06 | ack | 16 | syn | 26 | & | 36 | 6 | 46 | F | 56 | V | 66 | f | 76 | v
07 | bel | 17 | etb | 27 | ' | 37 | 7 | 47 | G | 57 | W | 67 | g | 77 | w
08 | bs | 18 | can | 28 | ( | 38 | 8 | 48 | H | 58 | X | 68 | h | 78 | x
09 | ht | 19 | em | 29 | ) | 39 | 9 | 49 | I | 59 | Y | 69 | i | 79 | y
0a | nl | 1a | sub | 2a | * | 3a | : | 4a | J | 5a | Z | 6a | j | 7a | z
0b | vt | 1b | esc | 2b | + | 3b | ; | 4b | K | 5b | [ | 6b | k | 7b | {
0c | np | 1c | fs | 2c | , | 3c | < | 4c | L | 5c | \ | 6c | l | 7c | ¦
0d | cr | 1d | gs | 2d | - | 3d | = | 4d | M | 5d | ] | 6d | m | 7d | }
0e | so | 1e | rs | 2e | . | 3e | > | 4e | N | 5e | ^ | 6e | n | 7e | ~
0f | si | 1f | us | 2f | / | 3f | ? | 4f | O | 5f | _ | 6f | o | 7f | del
n = 13, 占用了14个位置

## Slide 21: Trap Codes
LC-3 assembler provides “pseudo-instructions”(伪指令) for each trap code, so you don’t have to remember them.
Code | Equivalent | Description
HALT | TRAP x25 | Halt execution and print message to console.
IN | TRAP x23 | Print prompt on console, read (and echo) one character from keybd. Character stored in R0[7:0].
OUT | TRAP x21 | Write one character (in R0[7:0]) to console.
GETC | TRAP x20 | Read one character from keyboard. Character stored in R0[7:0].
PUTS | TRAP x22 | Write null-terminated string to console. Address of string is in R0.

## Slide 22: Style Guidelines
Use the following style guidelines to improve the readability and understandability of your programs:
  Provide a program header, with author’s name, date, etc.,and purpose of program.
  Start labels, opcode, operands, and comments in same column for each line. (Unless entire line is a comment.)
  Use comments to explain what each register does.
  Give explanatory comment(备注)for most instructions.
  Use meaningful symbolic names.
    Mixed upper and lower case for readability.
      ASCIItoBinary, InputRoutine, SaveR1
  Provide comments between program sections.
  Each line must fit on the page -- no wraparound or truncations.
    Long statements split in aesthetically (美学上) pleasing manner.

## Slide 23: Sample Program
Count the occurrences of a character in a file. Remember this?

## Slide 24: Program (1 of 2)
Address | Instruction | Comments
x3000 | 0 1 0 1 0 1 0 0 1 0 1 0 0 0 0 0 | R2  0 (counter) AND R2,R2, #0
x3001 | 0 0 1 0 0 1 1 0 0 0 0 1 0 0 0 0 | R3  M[x3012] (ptr) LD R3, x3012 (LD R3, PTR)
x3002 | 1 1 1 1 0 0 0 0 0 0 1 0 0 0 1 1 | Input to R0 (TRAP x23) TRAP x23 (GETC)
x3003 | 0 1 1 0 0 0 1 0 1 1 0 0 0 0 0 0 | R1  M[R3] LDR R1, R3, #0
x3004 | 0 0 0 1 1 0 0 0 0 1 1 1 1 1 0 0 | R4  R1 – 4 (EOT) ADD R4,R1, #-4
x3005 | 0 0 0 0 0 1 0 0 0 0 0 0 1 0 0 0 | If Z, goto x300E BRz x300E (BRz OUTPUT)
x3006 | 1 0 0 1 0 0 1 0 0 1 1 1 1 1 1 1 | R1  NOT R1 NOT R1,R1
x3007 | 0 0 0 1 0 0 1 0 0 1 1 0 0 0 0 1 | R1  R1 + 1 ADD R1,R1,#1
X3008 | 0 0 0 1 0 0 1 0 0 1 0 0 0 0 0 0 | R1  R1 + R0 ADD R1,R1,R0
x3009 | 0 0 0 0 1 0 1 0 0 0 0 0 0 0 0 1 | If N or P, goto x300B BRnp x300B (BRnp GETCHAR)

## Slide 25: Program (2 of 2)
Address | Instruction | Comments
x300A | 0 0 0 1 0 1 0 0 1 0 1 0 0 0 0 1 | R2  R2 + 1 ADD R2,R2,#1
x300B | 0 0 0 1 0 1 1 0 1 1 1 0 0 0 0 1 | R3  R3 + 1 ADD R3,R3,#1
x300C | 0 1 1 0 0 0 1 0 1 1 0 0 0 0 0 0 | R1  M[R3] LDR R1,R3,#0
x300D | 0 0 0 0 1 1 1 1 1 1 1 1 0 1 1 0 | Goto x3004 BRnzp x3004 (BRnzp TEST)
x300E | 0 0 1 0 0 0 0 0 0 0 0 0 0 1 0 0 | R0  M[x3013] LD R0,x3013 ( LD R0, ASCII)
x300F | 0 0 0 1 0 0 0 0 0 0 0 0 0 0 1 0 | R0  R0 + R2 ADD R0,R0,R2
x3010 | 1 1 1 1 0 0 0 0 0 0 1 0 0 0 0 1 | Print R0 TRAP x21 (OUT)
x3011 | 1 1 1 1 0 0 0 0 0 0 1 0 0 1 0 1 | HALT TRAP x25 (HALT)
X3012 | 1 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 | Starting Address of File (X9000)
x3013 | 0 0 0 0 0 0 0 0 0 0 1 1 0 0 0 0 | ASCII x30 (‘0’)

## Slide 26: Char Count in Assembly Language (1 of 3)
01 ;
02 ; Program to count occurrences of a character in a file.
03 ; Character to be input from the keyboard.
04 ; Result to be displayed on the monitor.
05 ; Program only works if no more than 9 occurrences are
06 ; found.
07 ;
08 ; Initialization
09 ;
0A .ORIG x3000
0B AND R2, R2, #0 ; R2 is counter, initially 0
0C LD R3, PTR ; R3 is pointer to characters
0D GETC ; TRAP x23
0E ; R0 gets character input
0F LDR R1, R3, #0 ; R1 gets first character
10 ;
11 ; Test character for end of file
12 ;
TEST ADD R4, R1, #-4 ; Test for EOT
; (ASCII x04)
15 BRz OUTPUT ; If done, prepare the output

## Slide 27: Char Count in Assembly Language (2 of 3)
16 ;
17 ; Test character for match. If a match, increment count.
18 ;
19 NOT R1, R1
1A ADD R1, R1, R0 ; If match, R1 = xFFFF
1B NOT R1, R1 ; If match, R1 = x0000
1C BRnp GETCHAR ; If no match, do not increment
1D ADD R2, R2, #1
1E ;
1F ; Get next character from file.
20 ;
21 GETCHAR ADD R3, R3, #1 ; Point to next character.
22 LDR R1, R3, #0 ; R1 gets next char to test
23 BRnzp TEST
24 ;
25 ; Output the count.
26 ;
27 OUTPUT LD R0, ASCII ; Load the ASCII template
28 ADD R0, R0, R2 ; Covert binary count to ASCII
29 OUT ; TRAP x21
2A ; ASCII code in R0 is displayed.
2B HALT ; TRAP x25,Halt machine

## Slide 28: Char Count in Assembly Language (3 of 3)
2C ;
2D ; Storage for pointer and ASCII template
2E ;
2F ASCII .FILL x0030
30 PTR .FILL x9000
31 .END

## Slide 29
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary
Review
1
3
Assembly Process
2
Assembly Language Overview
4
Summary

## Slide 30: Assembly Process
Convert assembly language file (.asm) into an executable file (.obj) for the LC-3 simulator.
First Pass:
  scan program file
  find all labels and calculate the corresponding addresses; this is called the symbol table
Second Pass:
  convert instructions to machine language, using information from symbol table

## Slide 31: First Pass: Constructing the Symbol Table
Find the .ORIG statement, which tells us the address of the first instruction.
  Initialize location counter (LC), which keeps track of the current instruction.
For each non-empty line in the program:
  If line contains a label, add label and LC to symbol table.
  Increment LC.
    NOTE: If statement is .BLKW or .STRINGZ, increment LC by the number of words allocated.
Stop when .END statement is reached.
NOTE: A line that contains only a comment is considered an empty line.

## Slide 32: Example
Construct the symbol table for the program in Figure 7.2
Symbol | Address
TEST | X3004
GETCHAR | X300B
OUTPUT | X300E
ASCII | X3012
PTR | X3013

## Slide 33: Second Pass: Generating Machine Language
For each executable assembly language statement, generate the corresponding machine language instruction.
  If operand is a label, look up the address from the symbol table.
Potential problems:
  Improper number or type of arguments
    ex: NOT R1,#7 ADD R1,R2 ADD R3,R3,NUMBER
  Immediate argument too large
    ex: ADD R1,R2,#1023
  Address (associated with label) not on the same page 被访问的标号地址不在当前指令直接寻址的范围之内
    can’t use direct addressing mode

## Slide 34: Practice
Statement | Machine Language
LD R3,PTR | 
ADD R4,R1,#-4 | 
LDR R1,R3,#0 | 
BRnp GETCHAR | 
Using the symbol table constructed earlier, translate these statements into LC-3 machine language.
(Assume all addresses are on the current page.)

## Slide 35: Practice
Statement | Machine Language
LD R3,PTR | 0010 011 000010001
ADD R4,R1,#-4 | 0001 100 001 1 11100
LDR R1,R3,#0 | 0110 001 011 000000
BRnp GETCHAR | 0000 101 000000001
Using the symbol table constructed earlier, translate these statements into LC-3 machine language.
(Assume all addresses are on the current page.)

## Slide 36: LC-3 Assembler
Using “assemble” (Unix) or LC3 Edit (Windows), generates several different output files.
This one gets loaded into the simulator.

## Slide 37: Object File Format
LC-3 object file contains
  Starting address (location where program must be loaded), followed by…
  Machine instructions
Example
  Beginning of “count character” object file looks like this:
0011000000000000 0101010010100000 0010011000010100 1111000000100011 . . .
.ORIG x3000
AND R2, R2, #0
LD R3, PTR
TRAP x23

## Slide 38: Multiple Object Files
An object file is not necessarily a complete program.
  system-provided library routines
  code blocks written by multiple developers
For LC-3, can load multiple object files into memory, then start executing at a desired address.
  system routines, such as keyboard input, are loaded automatically
    loaded into “system memory,” below x1000
    by convention, user code should be loaded between x3000 and xCFFF
  each object file includes a starting address
  be careful not to load overlapping object files

## Slide 39: Linking and Loading
Loading is the process of copying an executable image into memory.
  more sophisticated loaders are able to relocate images to fit into available memory
  must readjust (重新适应) branch targets, load/store addresses
Linking is the process of resolving symbols between independent object files.
  suppose we define a symbol in one module, and want to use it in another
  some notation, such as .EXTERNAL, is used to tell assembler that a symbol is defined in another module
  linker will search symbol tables of other modules to resolve symbols and complete code generation before loading

## Slide 40
Outline
Review
1
3
A Machine Structure：von Neumann Model
2
From ENIAC to the Stored Program Computer
4
Summary
Review
Assembly Process
Assembly Language Overview
4
Summary

## Slide 41
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Summary: Assembly Language
Now, You are Here.
ALUOP[0:3] <= InstReg[9:11] & MASK

## Slide 42: Memory map of the LC-3
PC
R4(Global pointer)
R6 (stack pointer)
Device Register
Addresses
0x0000
0xFFFF
Trap Vector Table
Interrupt Vector Table
Operating System
and Supervisor Stack
0x00FF
0x0100
0x01FF
0x0200
0x2FFF
0x3000
0xFDFF
0xFE00
Run-time stack
Program Text
Global data section
Heap (for dynamically
allocated memory)
R5 (frame pointer)
R5
Function2
R6
R5
R6
Function3
Function1
R5
R6