## Slide 1: Chapter 9-2 Operating System Service Routines
计算机科学与技术学院
School of Computer Science and Technology
计算系统概论A
Introduction to Computing Systems
（ CS1002A.01 ）

## Slide 2
Outline
Review
1
3
A Machine Structure：von Neumann Model
Review
1
3
Operating System Service Routines
Review
1
TRAP Routines
2

## Slide 3: Today: CONTROL in Von Neumann Model

## Slide 4: Control Instructions for System Calls
1
1
1
1
0
0
0
0
TrapVector8
TRAP
0
0
0
0
n
z
p
PCoffset9
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
0
1
0
0
1
PCoffset11
0
1
0
0
0
0
0
BaseR
0
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
BR
JSRR
RTI
JSR
1
1
0
0
0
0
0
BaseR
0
0
0
0
0
0
JMP
1
1
0
0
0
0
0
1
1
1
0
0
0
0
0
0
RET

## Slide 5
SR2
3
SR2MUX
16
16
16
16
[10:0]
16
16
SEXT
SEXT
SEXT
[8:0]
[5:0]
[4:0]
SEXT
INPUT
MEM.EN,R,W
16
MAR
16
LD.MAR
PC
GatePC
OUTPUT
MEMORY
MUX
MUX
MDR
…
+
16
16
16
16
ADDR1MUX
2
PCMUX
+1
16
MARMUX
SEXT
[7:0]
GateMARMUX
LD.PC
16
16
16
ADDR2MUX
16
LD.MDR
MUX
MIO.EN
GateMDR
16
16
16
ALU
A
B
ALUK
2
FINITE STATE MACHINE
N
Z
P
RUN
LD.IR
IR
16
DR
LD.REG
REG FILE
SR1
OUT
SR2
OUT
3
3
16
16
GateALU
SR1
LOGIC
16
LD.CC
Today: CONTROL in LC-3 Data Path
Control Unit

## Slide 6
Outline
Review
1
3
A Machine Structure：von Neumann Model
Review
1
3
Operating System Service Routines
Review
1
TRAP Routines
2

## Slide 7: System Calls
Some operations require specialized knowledge and protection
  Understanding IO device registers and how to use them poses a challenge to most application programmers.
  I/O registers are shared by many programs, and in general it is
  ill-advised (不明智的) to give user programmers access to these registers.
Solution: service routines or system calls
  Low-level, privileged operations performed by operating system
    1. User program invokes (调用) system call
    2. Operating system code:
      Saves registers
      Performs operation
      Restores registers
    3. Returns control to user program

## Slide 8: LC-3 TRAP Mechanism
Provides a set of service routines
  Part of operating system
  routines start at arbitrary (任意) addresses
  Up to 256 (why?) routines
Requires a table of starting addresses
  Stored in memory (x0000 through x00FF)
  Used to associate code with trap number
  Called Trap Vector Table (or System Control Block)
Uses the TRAP instruction
  When a user program wishes to
  have the operating system execute a specific service routine on behalf of the user program
  and then return control to the user program
Uses a linkage mechanism
  For returning control to the user program
  Execution resumes immediately after the TRAP instruction
  Routines use the RTI instruction

## Slide 9: LC-3 TRAP Routines(service routines)
  GETC (TRAP x20)
    Read a single character from keyboard.
    The character is not echoed to the console.
    ASCII copied into R0 and R0[15:8] is cleared.
  OUT (TRAP x21)
    Write R0[7:0] to the console display.
  PUTS (TRAP x22)
    Write a string of ASCII characters to the console display.
    String address in R0.
    Writing terminates with the occurrence of x0000
  IN (TRAP x23)
    Print a prompt on the screen and read a single character from the keyboard.
    Character is echoed to the console. .
    ASCII copied into R0 and R0[15:8] is cleared.
  HALT (TRAP x25)
    Halt execution and print a message on the console.
:
x0400
x0430
x0450
x04A0
x04E0
x0520
x0000
:
x0020
x0021
x0022
x0023
x0024
x0025
:
:
x00FF
The LC-3 Trap Vector Table
预留代码空间
(实用代码空间)
:
48
32(14)
96
64(42)
:

## Slide 10: TRAP Instruction
1 1 1 1
15 14 13 12
11 10 9 8
7 6 5 4 3 2 1 0
0 0 0 0
trap vector
Trap vector
  Identifies which service routine the user program wants the operating system to execute on its behalf
  8-bit trap vector zero-extended to form 16-bit address, serves as index into table of service routine addresses
Where to go
  Lookup starting address from table
Enabling return
  Push the address of next instruction after TRAP together with the PSR to the system stack (Poped by the RTI instruction)
TRAP
:
x0400
x0430
x0450
x04A0
x04E0
x0520
x0000
:
x0020
x0021
x0022
x0023
x0024
x0025
:
:
x00FF
The LC-3 Trap Vector Table

## Slide 11: TRAP Mechanism Operation
①
②
③
RTI

## Slide 12: TRAP Mechanism Operation

## Slide 13: TRAP Mechanism Operation
  OLD_PSR=PSR;
  if (PSR[15] == 1) { // called by a user program
  Saved_USP  R6;
  R6  Saved_SSP; //SSP：系统栈指针
  }
  PSR[15]=0; // switch to supervisor mode
  Push OLD_PSR, PC+1 on the system stack
  PC = mem[ZEXT(trapvect8)]; // set PC
  PSR[15]=0 means supervisor privilege, and PSR[15]=1 means unprivileged.

## Slide 14: RTI instruction
RTI instruction – Return from Trap or Interrupt
1 0 0 0
15 14 13 12
11 10 9 8 7 6
5 4 3 2 1 0
0000 0000 0000
RTI

## Slide 15: RTI instruction
// now ,we need to be in the supervisor mode
if (PSR[15] == 1) // which means we are in the user mode
//RTI cannot be called by user program
Initiate a privilege mode exception;
else
PC = mem[R6]; // R6 is the SSP, PC is restored
R6 = R6+1;
OLD_PSR = mem[R6]; // OLD_PSR is restored
R6 = R6+1; //system stack completes POP before saved PSR //is restored
PSR = OLD_PSR ; //PSR is restored
if (PSR[15] == 1) // supervisor mode  user mode
saved_SSP=R6;
R6=Saved_USP;

## Slide 16: An example of using TRAP
.ORIG x3000
LD R2,TERM ; Load –’7’
LD R3,ASCII ; Load ASCII difference
AGAIN TRAP x23 ; Request keyboard input
ADD R1,R2,R0 ; Test for terminating
BRz EXIT ; character
ADD R0,R0,R3 ; Change to lowercase
TRAP x21 ; Output to the monitor
BRnzp AGAIN ; ... and do it again!
TERM .FILL xFFC9 ; FFC9 is negative of ASCII ‘7’
ASCII .FILL x0020
EXIT TRAP x25 ; Halt
.END

## Slide 17
Outline
Review
1
3
A Machine Structure：von Neumann Model
Review
1
3
Operating System Service Routines
Review
1
TRAP Routines
2

## Slide 18: Character Input Service Routine (IN, TRAP x23)
01 ; Service Routine for Keyboard Input
02 ;
03 .ORIG x04A0
04 START ST R1,SaveR1 ; Save the values in the registers
05 ST R2,SaveR2 ; that are used so that they
06 ST R3,SaveR3 ; can be restored before RTI
07 ;
08 LD R2,Newline ; Newline: ASCII code for newline x000A
09 L1 LDI R3,DSR ; Check DDR -- is it free?
0A BRzp L1 ; Display is free when DSR is negative
0B STI R2,DDR ; Move cursor to new clean line
0C ;
0D LEA R1,Prompt ; Prompt is starting address
0E ; of prompt string
1F Loop LDR R0,R1,#0 ; Get next prompt character
10 BRz Input ; Check for end of prompt string, nul
11 L2 LDI R3,DSR ; Check DDR -- is it free?
12 BRzp L2
13 STI R0,DDR ; Write next char
14 ; prompt string
15 ADD R1,R1,#1 ; Increment prompt pointer
16 BRnzp Loop
17 ;
  IN (TRAP x23)
    Print a prompt on the screen and read a single character from the keyboard.
    Character is echoed to the console. .
    ASCII copied into R0 and R0[15:8] is cleared.

## Slide 19: Character Input Service Routine (IN, TRAP x23)
18 Input LDI R3,KBSR ; Has a character been typed?
19 BRzp Input ; When typed, KBSR is negative
1A LDI R0,KBDR ; Load it into R0
1B L3 LDI R3,DSR
1C BRzp L3 ; Display is free when DSR is negative
1D STI R0,DDR ; Echo input character
1E ; to the monitor
1F ;
20 L4 LDI R3,DSR
21 BRzp L4 ; Display is free when DSR is negative
22 STI R2,DDR ; Move cursor to new clean line
23 LD R1,SaveR1 ; Service routine done, restore
24 LD R2,SaveR2 ; original values in registers.
25 LD R3,SaveR3
26 RTI ; Return from Trap
27 ;
28 SaveR1 .BLKW 1
29 SaveR2 .BLKW 1
2A SaveR3 .BLKW 1
2B DSR .FILL xFE04
2C DDR .FILL xFE06
2D KBSR .FILL xFE00
2E KBDR .FILL xFE02
2F Newline .FILL x000A ; ASCII code for newline
30 Prompt .STRINGZ "Input a character>"
31 .END
  IN (TRAP x23)
    Print a prompt on the screen and read a single character from the keyboard.
    Character is echoed to the console. .
    ASCII copied into R0 and R0[15:8] is cleared.

## Slide 20: A String Output Service Routine (OUT,TRAP x21)
01 .ORIG x0420 ; System call starting address
02 ST R1, SaveR1 ; R1 will be used to poll the DSR
03 ; hardware
04 ; Write the character
05 TryWrite LDI R1, DSR ; Get status
06 BRzp TryWrite ;Display is free when DSR is negative
07 WriteIt STI R0, DDR ; Write character
08
09; return from trap
0A Return LD R1, SaveR1 ; Restore registers
0B RTI ; Return from trap
0C DSR .FILL xFE04 ; Address of display status register
0D DDR .FILL xFE06 ; Address of display data register
0E SaveR1 .BLKW 1
0F .END
  OUT (TRAP x21)
    Write R0[7:0] to the console display.

## Slide 21: A String Output Service Routine (PUTS,TRAP x22)
05 .ORIG x0460
06 ST R0, SaveR0 ; Save registers that
07 ST R1, SaveR1 ; are needed by this
08 ST R3, SaveR3 ; trap service routine
0A ; Loop through each character in the array
0C Loop LDR R1, R0, #0 ; Retrieve the character(s)
0D BRz Return ; If it is 0, done
0E L2 LDI R3,DSR
0F BRzp L2 ;Display is free when DSR is negative
10 STI R1, DDR ; Write the character
11 ADD R0, R0, #1 ; Increment pointer
12 BRnzp Loop ; Do it all over again
13 ;
14 ; Return from the request for service call
15 Return LD R3, SaveR3
16 LD R1, SaveR1
17 LD R0, SaveR0
18 RTI
19 ;
1A ; Register locations
1B DSR .FILL xFE04
1C DDR .FILL xFE06
1D SaveR0 .FILL x0000
1E SaveR1 .FILL x0000
1F SaveR3 .FILL x0000
20 .END
  PUTS (TRAP x22)
    Write a string of ASCII characters to the console display.
    String address in R0.
    Writing terminates with the occurrence of x0000

## Slide 22: Halt the machine(HALT,TRAP x25)
01 .ORIG x0520 ; Where this routine resides
02 ST R1, SaveR1 ; R1: a temp for MC register
03 ST R0, SaveR0 ; R0 is used as working space
04
05 ; print message that machine is halting
06
07 LD R0, ASCIINewLine ;out x000A
08 TRAP x21
09 LEA R0, Message ;puts “Halting the machine."
0A TRAP x22
0B LD R0, ASCIINewLine ;out x000A
0C TRAP x21
0D ;
0E ; clear bit 15 at xFFFE (Master Control Register, MCR )to stop the machine, i.e., MCR[15] = 0
0F ;
10 LDI R1, MCR ; Load MC register into R1
11 LD R0, MASK ; R0 = x7FFF
12 AND R0, R1, R0 ; Mask to clear the top bit
13 STI R0, MCR ; Store R0 into MC register
  HALT (TRAP x25)
    Halt execution and print a message on the console.

## Slide 23: Halt the machine(HALT,TRAP x25)
14 ;
15 ; return from HALT routine.
16 ; (how can this routine return if the machine is halted above?)
17 ;
18 LD R1, SaveR1 ; Restore registers
19 LD R0, SaveR0
1A RTI
1B ;
1C ; Some constants
1D ;
1E ASCIINewLine .FILL x000A
1F SaveR0 .BLKW 1
20 SaveR1 .BLKW 1
21 Message .STRINGZ "Halting the machine."
22 MCR .FILL xFFFE ; Address of MCR
23 MASK .FILL x7FFF ; Mask to clear the top bit
24 .END
  HALT (TRAP x25)
    Halt execution and print a message on the console.

## Slide 24: Using subroutines to implement (IN, TRAP x23)
01 .ORIG x04A0
02 START JSR SaveReg
03 LD R2,Newline
04 JSR WriteChar
05 LEA R1,PROMPT
06 ;
07 ;
08 Loop LDR R2,R1,#0 ; Get next prompt char
09 BRz Input
0A JSR WriteChar
0B ADD R1,R1,#1
0C BRnzp Loop
0D ;
……
1A WriteChar
LDI R3,DSR
1B BRzp WriteChar
1C STI R2,DDR
1D RET ; JMP R7 terminates subroutine
1E DSR .FILL xFE04
1F DDR .FILL xFE06
20 ;
……
  IN (TRAP x23)
    Print a prompt on the screen and read a single character from the keyboard.
    Character is echoed to the console. .
    ASCII copied into R0 and R0[15:8] is cleared.

## Slide 25: Using Traps to implement (IN, TRAP x23)

## Slide 26: Data Type Conversion
I/O
  Keyboard input routines read ASCII characters (not binary values)
  Console output routines write ASCII (‘s’ not “x73”)
Consider this program:
TRAP x23 ; input from keyboard ADD R1, R0, #0 ; move to R1 TRAP x23 ; input from keyboard ADD R0, R1, R0 ; add two inputs TRAP x21 ; display result TRAP x25 ; HALT
User inputs ‘2’ and ‘3’ -- what happens?
Result displayed: ‘e’
Why?
  ASCII '2' (x32) + ASCII '3' (x33) = ASCII 'e' (x65)

## Slide 27: ASCII to Binary
Single digit numbers are trivial (subtract x30)
  E.g., ‘7’ is ASCII x37, x37 - x30 = x7
Input
  Assume we've read three ASCII digits (e.g., "259") into a memory buffer
How do we convert this to a number we can use?
  Convert first character to digit (subtract x30) and multiply by 100
  Convert second character to digit and multiply by 10
  Convert third character to digit
  Add the three digits together

## Slide 28: ASCII to Binary Conversion Algorithm

## Slide 29: Multiplication
How can we multiply a number by 10?
  Approach 0
    Use the MUL instruction
  Approach 1
    Add <number> to itself 10 times
  Approach 2
    Add 10 to itself <number> times (better if number < 10)
  Approach 3
    Look it up! Only practical if number of multiplicands is small

## Slide 30: Code for Lookup Table
; multiply R0 by 100, using lookup table
; LEA R1, Lookup100 ; R1 = table base ADD R1, R1, R0 ; add index (R0) LDR R0, R1, #0 ; load from M[R1] ... Lookup100 .FILL #0 ; entry 0 .FILL #100 ; entry 1 .FILL #200 ; entry 2 .FILL #300 ; entry 3 .FILL #400 ; entry 4 .FILL #500 ; entry 5 .FILL #600 ; entry 6 .FILL #700 ; entry 7 .FILL #800 ; entry 8 .FILL #900 ; entry 9

## Slide 31: Complete ASCII to Binary Conversion Code
ASCII "259” to value 259
ASCIIBUF
3
R1

## Slide 32: Complete ASCII to Binary Conversion Code (1 of 3)
; Three-digit buffer at ASCIIBUF.
; R1 tells how many digits to convert.
; Put resulting decimal number in R0.
ASCIItoBinary AND R0, R0, #0 ;clear result ADD R1, R1, #0 ;test # digits BRz DoneAtoB ;done if no digits
; LD R3, NegZero ;R3 = -x30 LEA R2, ASCIIBUF ;ptr to the first digit ADD R2, R2, R1 ;R2 =(R2)+(R1) ADD R2, R2, #-1 ;points to ones digit
; LDR R4, R2, #0 ;load digit ADD R4, R4, R3 ;convert to number ADD R0, R0, R4 ;add ones contribution
;

## Slide 33: Complete ASCII to Binary Conversion Code(2 of 3)
ADD R1, R1, #-1 ;one less digit BRz DoneAtoB ;done if zero ADD R2, R2, #-1 ;points to tens digit
;
LDR R4, R2, #0 ;load ‘tens’ digit ADD R4, R4, R3 ;convert to number LEA R5, Lookup10 ;multiply by 10 ADD R5, R5, R4 LDR R4, R5, #0 ADD R0, R0, R4 ;adds tens contribution to total
; ADD R1, R1, #-1 ;one less digit BRz DoneAtoB ;done if zero ADD R2, R2, #-1 ;points to hundreds digit
;
LDR R4, R2, #0 ;load digit ADD R4, R4, R3 ;convert to number LEA R5, Lookup100 ;multiply by 100 ADD R5, R5, R4 LDR R4, R5, #0 ADD R0, R0, R4 ;adds 100's contrib

## Slide 34: Complete ASCII to Binary Conversion Code(3 of 3)
DoneAtoB RET
NegZero .FILL xFFD0 ;-x30
ASCIIBUF .BLKW 4
Lookup10 .FILL #0 .FILL #10 .FILL #20 ...
Lookup100 .FILL #0 .FILL #100 .FILL #200
...

## Slide 35: Binary to ASCII Conversion
Converting a 2's complement binary value to a three-digit decimal number
  Resulting characters can be output using OUT
Instead of multiplying, we need to divide by 100 to get hundreds digit.
  Why wouldn't we use a lookup table for this problem?
  Subtract 100 repeatedly from number to divide.
First, check whether number is negative.
  Write sign character (+ or -) to buffer and make positive.

## Slide 36: Binary to ASCII Conversion Code (1 of 3)
; R0 is between -999 and +999.
; Put sign character in ASCIIBUF, followed by three
; ASCII digit characters.
BinaryToASCII LEA R1, ASCIIBUF ;ptr to result string ADD R0, R0, #0 ;test sign of value BRn NegSign LD R2, ASCIIplus ;store '+' STR R2, R1, #0 BR Begin100
NegSign LD R2, ASCIIneg ;store '-' STR R2, R1, #0 NOT R0, R0 ;convert value to pos ADD R0, R0, #1
Begin100 LD R2, ASCIIoffset LD R3, Neg100
Loop100 ADD R0, R0, R3 BRn End100 ADD R2, R2, #1 ;add one to digit BR Loop100

## Slide 37: Binary to ASCII Conversion Code(2 of 3)
End100 STR R2, R1, #1 ;store ASCII 100's digit LD R3, Pos100 ADD R0, R0, R3 ;restore last subtract
; LD R2, ASCIIoffset LD R3, Neg10
Loop10 ADD R0, R0, R3 BRn End10 ADD R2, R2, #1 ;add one to digit BR Loop10
End10 STR R2, R1, #2 ;store ASCII 10's digit ADD R0, R0, #10 ;restore last subtract
; LD R2, ASCIIoffset ADD R2, R2, R0 ;convert one's digit STR R2, R1, #3 ;store one's digit RET
;

## Slide 38: Binary to ASCII Conversion Code(3 of 3)
ASCIIplus .FILL x002B ;plus sign ASCII code
ASCIIneg .FILL x002D ;neg sign ASCII code
ASCIIoffset .FILL x0030 ;zero’s ASCII code
Neg100 .FILL xFF9C ;-100
Pos100 .FILL x0064 ;100
Neg10 .FILL xFFF6 ;-10